## Slide 1
Flash memory - Physical addressable memory within flash core
array
Flash Module - Flash core and interface circuit (Wrapper)
Flash Core - Memory Arrays, I/O buffers, read and program
data path and associated control logic
Flash segment - Contiguous blocks of memory cells which, when
when added together, create the memory array
Wrapper - Interface circuitry between Flash core and
cDSP
Charge pump - Voltage generators and associated control logic
F206 device flash Terminology
Ver.1.10

## Slide 2
Flash Memory Features
Flash array Organization : Flash0 16k word - 0000h -3FFFh
Flash1 16k word - 4000h -7FFFh
Power supply : 5v only( 4.9v to 5.10v)
Erase segment size : 8 segments maximum
2k byte minimum segment size
Access time : 1clock cycle
Instruction time : 50ns
Memory functions : Read/ Erase/ Program/ controlled by cDSP core
Algorithm length : 1K words of DSP code
(Clear, Erase,Writing )

## Slide 3
Stages of Flash bit programming
1. Clearing - Write 0 in all bits
2. Erasing - Write 1 in all bits
3. Write/Coding - Write 0 in selected bits
Flash Programming Sequence

## Slide 4
F_ACCESS0 register
at IO address -0xffe0
F_ACCESS1 register
at IO address -0xffe1
Flash0 array - 0x0000h- 3fffh
Flash1 array - 0x4000h- 7fffh
Bit0
Bit0
Bit0 Flash Mode Function Reset value
1 Array mode Normal memory access 1
0 Register mode Flash array programming
F206
DSP Core
Address bus
Databus
16k word flash array
2kx8 segments
16k word flash array
2kx8 segments
F_ACCESS register control functions
32kx16 Flash Array control logic

## Slide 5
On_chip Flash programming interface
PC/ Sun
XDS510
F206
Target #1
Emulation / Debugger
JTAG port
Pod

## Slide 6
B0 - Memory map used for Flash programming using
JTAG loader PRG2XXW.EXE
0x60 -0x69h
0x6a -0x7fh
Variables for JTAG
communication utility
B2 -DARAM
B1 -DARAM
B0 -DARAM
Flash0 array
0x0000h- 0x3fffh
0x300-0x30fh
0xff00h
0xffffh
Flash1 array
0x4000h- 0x7fffh
Program code in program space Data variables and flash code Flash code destination
Flash0 or Flash1 array
Not used
0x310-0x31fh
0x320-0x3e7h
Variables for C2xxprog
and flash algorithms
Data space used to store
flash code to be flashed
in blocks 200 words
Program code space used
to run flash algorithms
and control code for flash
array clear, erase and
programming.
Each function should be
256 words max
Temporary variables
for flash algorithms

## Slide 7
B0 Memory variables and functions used in Flash programming using JTAG loader PRG2XXW.EXE
0x60 -0x69h
PRG_parm
0x310 -0x31fh
Variables for JTAG
B2 -DARAM
B1 -DARAM
B0 -DARAM
Flash0 array
0x0000h- 0x3fffh
0x320h
Flash code space
Blocks of
200 words
0xff00h
0xffffh
Flash1 array
0x4000h- 0x7fffh
Program code in program space Data variables and flash code Flash code destination
Flash0 or Flash1 array
PRG_paddr
PRG_bufaddr
PRG_bufsize
PRG_paddr
PRG_length
PRG_length
0x300 -0x30fh
Variables for C2xxprog
and flash algorithms
0x6a -0x7fh
Not used
Program code space used
to run flash algorithms
and control code for flash
array clear, erase and
programming.
Each function should be
256 words max
Temporary variables
for flash algorithms

## Slide 8
SARAM - Memory map used for Flash programming using
JTAG loader PRG2XXW.EXE
0x60 -0x69h
0x6a -0x7fh
Variables for JTAG
communication utility
B2 -DARAM
B1 -DARAM
SARAM in PM space
Flash0 array
0x0000h- 0x3fffh
0x300-0x30fh
0xC00h
0x03cfh
Flash1 array
0x4000h- 0x7fffh
Program code in program space Data variables Flash code destination
and flash code in Data space Flash0 or Flash1 array
Not used
0x310-0x31fh
0x320-0x3ffh
Not used
0x8000-0x83ffh
SARAM in DM space
Data space used to store
flash code to be flashed
in blocks 2000 words
Not used
Variables for C2xxprog
and flash algorithms
Program code space used
to run flash algorithms
and control code for flash
array clear, erase and
programming.
1024 words max.
Temporary variables
for flash algorithms

## Slide 9
SARAM Memory variables and functions used in Flash programming using JTAG loader PRG2XXW.EXE
0x60 -0x69h
PRG_parm
0x310 -0x30fh
Variables for JTAG
B2 -DARAM
B1 -DARAM
SARAM in PM space
Flash0 array
0x0000h- 0x3fffh
0x8000h
0xC00h
Flash1 array
0x4000h- 0x7fffh
Program code in program space Data variables Flash code destination
and flash code in data space Flash0 or Flash1 array
PRG_paddr
PRG_bufaddr
PRG_bufsize
PRG_paddr
PRG_length
PRG_length
0x300 -0x30fh
Variables for C2xxprog
and flash algorithms
0x6a -0x7fh
Not used
SARAM in DM space
Flash code space
Blocks of
2000 words
Program code space used
to run flash algorithms
and control code for flash
array clear, erase and
programming.
1024 words max.
Temporary variables
for flash algorithms

## Slide 10
Flash array variables used by Flash algorithms and JTAG loader
0x60 -0x69h
PRG_parm
0x310 -0x30fh
Variables for JTAG
B2 -DARAM
B1 -DARAM
0x300 -0x30fh
Variables for C2xxprog
and flash algorithms
0x6a -0x7fh
Not used
PRG_parm at 0x310 -0x30fh
--------------------------------------
0x0310h - PRG_bufaddr - Used by JTAG loader
0x0311h - PRG_bufsize - Used by JTAG loader
0x0312h - PRG_devsize - Used by JTAG loader
0x0313h - PRG_paddr - Defined and used by JTAG loader
0x0314h - PRG_page - Reserved
0x0315h - PRG_length - Defined and used by JTAG loader
0x0316h - PRG_status - Used by JTAG loader
0x0317h - Temp - Reserved
0x0318h - PROTECT - Segment protect used by algorithms
0x0319h - FL_ST - Segment start address used by algorithms
0x031ah - FL_END - Segment end address used by algorithms
0x031bh - FL_LEN - Segment length used by algorithms
0x0310ch - PRG_END - Reserved
Temporary variables
for flash algorithms

## Slide 11
Control Registers Address Description
SEG_CTR 0 Segment control register. The most significant 8- bits enable specific segments
for erasure or programmation. Setting a bit to 1 enables the segment.
The least significant bits control the program, erase and verify
operations of the segments
TST 1 Reserved for test.
WADRS 2 Write address. Holds address during write operation
WDATA 3 Write data. Hold data during write operation
Flash control registers in register mode

## Slide 12
Segment control register SEG_CTR
Name Bit address Active Description
EXE 0 1 Execute. This bit initiates and ends programming and erasing of the flash array.
EXE and KEY 0/1 bits must be written in the same write access. This protocol is
to be followed for programmation to occur. After the required programming time
the EXE bit should be cleared in the same write as KEY0/1 bits. The data and
address latches are locked whenever the EXE bit is set and all attempts to read
from or write to the array will be ignored.
ERASE 1 1 Initiates erasure setup. Set this bit to perform the erase operation. The ERASE
bit must be set prior to setting EXE bit.
WRITE 2 1 Enable write logic. Set this bit to perform a write operation. The WRITE bit must
set prior to setting EXE bit.
VER1 3 1 Verify 1 mode. Proper erasure and programmation levels are acheived by
monitoring these bits
VER0 4 1 Verify 0 mode
KEY0 5 0 Execute key bits .These bits must be written as 01 in the same access as EXE bit
KEY1 6 1 for EXE operation to start. These bits are used as additional protection against
inadvertent programmation or erasure of the flash. These bits are read as zeros.
BUSY 7 Reserved
SEG7-0 15-8 1 Segment enable bits. Each segment enable bit individually protects or enables write
and erase operation for each of the segments in the flash array. Bit 8 controls
segment 0 and bit 15 controls the segment 7 of the flash array

## Slide 13
BUSY
KEY 1
KEY 0
VER 0
VER 1
WRITE
ERASE
EXE
8
15
0
1
2
3
4
5
6
7
Segment control register - SEG_CTR 0x0000h 0x4000h
TEST register - Reserved - TST 0x0001h 0x4001h
WRITE Address register - WADRS 0x0002h 0x4002h
WRITE Data register - WDATA 0x0003h 0x4003h
Flash Wrapper/ Control Registers Flash0 registers - Flash1 registers
Segment control bits
cDSP CORE
Charge Pump and Control
Flash Segment 0 - 2k words
Flash Segment 7- 2k words
16k word Flash core interface
Flash Core 2kx8 = 16k words