## Slide 1
TMS320C54x DSP Architecture and Software Development Tools
Notes: 1
In this module, we will review the C54x architecture and discuss the software tools available to speed development of DSP applications.

## Slide 2
Agenda
Review architecture
Introduce C54x tools
  Code generation tools
  Software development tools
Highlight the DSKplus
Notes: 2
We will review the architecture with an emphasis on functionality, then introduce the code generation & software development tools. Our discussion will include the C compiler, the assembly linker, and other debug tools such as the simulator. We will also highlight the C54x DSKplus, a useful demonstration board with a wide variety of capabilities.

## Slide 3
Objectives
Describe the C54x architecture components and functions
Recognize the code generation & debug tools and their functions
Recognize the software tools’ process flows
Identify the DSKplus demo board capabilities
Notes: 3
By the time you complete this module, you will be able to describe the C54x architecture and its components, recognize the code generation and debug tools and their functions, and understand the software development flow using these tools. You will also be aware of the capabilities of the C54x DSKplus demonstration board, and other development tools.

## Slide 4
C54x Architecture
OPTIMIZED CORE
JTAG TEST/ EML CONTROL
ROM
RAM
POWER
MGMT
PROGRAM / DATA BUSES
PERIPHERAL BUS
D(15-0)
A(15-0)
PERIPHERALS
Notes: 4
Here we see the C54x architecture.
The CPU (optimized core) is shown in the lower left, and is attached to the rest of the device through the bus structure, including program and data buses, and peripheral bus. Along the top we see RAM and ROM, power management functions, and emulation control. The C54x also offers a broad myriad of peripherals. Let’s examine the components in more detail.

## Slide 5
OPTIMIZED CORE
JTAG TEST/ EML CONTROL
ROM
RAM
POWER
MGMT
PROGRAM / DATA BUSES
PERIPHERAL BUS
D(15-0)
A(15-0)
PERIPHERALS
C54x Architecture
Notes: 5
We begin with the optimized CPU core.

## Slide 6
C54x Optimized Core
TO BUSES
MAC
ALU
17 X 17 MPY
40 BIT ADDER
RND, SAT
40 BIT ALU
CMPS OPERATOR (VITERBI)
EXP ENCODER
SHIFTER
ACCUMULATORS
40 BIT BARREL
(- 16, 31)
40 BIT ACC A
40 BIT ACC B
ADDRESSING UNIT
8 AUXILIARY REGISTERS
2 ADDRESSING UNITS
Notes: 6
The optimized CPU core has several components. The first and probably most important, is the multiply / accumulator or MAC. This particular device of the C54x family has a 17 X 17 multiplier rather than a 16 X 16 which is used on some other DSP product families. This enables unsigned by unsigned multiplication, signed by signed multiplication, and mixed-mode multiplication. It contains a 40-bit adder with 32-bit results and 8 bits of guard band and rounding & saturation control.
In addition, we see a 40-bit ALU which is capable of doing two 16-bit ALU operations. There's also a compare select store unit, the CMPS operator. This portion of the core allows you to accelerate Viterbi operations. There's an exponent encoder and two 40-bit accumulators. This differs from previous TI DSP families in that in the past we've had a single accumulator and in some cases an accumulator buffer.
Finally, we see a 40-bit barrel shifter and an addressing unit which houses eight auxiliary registers with two address generation units.

## Slide 7
OPTIMIZED CORE
JTAG TEST/ EML CONTROL
ROM
RAM
POWER
MGMT
PROGRAM / DATA BUSES
PERIPHERAL BUS
D(15-0)
A(15-0)
PERIPHERALS
C54x Architecture
Notes: 7
The core is connected to the other features of the device through it’s bus structure.

## Slide 8
C54x Internal Buses
PROGRAM / DATA BUSES
PERIPHERAL BUS
TO MEMORY
TO CORE
TO PERIPHERALS
D(15-0)
A(15-0)
Notes: 8
There are four main buses for data and instruction movement: the program bus (or instruction bus), and three data buses, two for reads and one for writes.
The bus structure also include four additional buses: the peripheral bus, two accumulator buses, and a multiplier bus.
The accumulator & multiplier buses can be thought of as a data highway. We need to move data from the accumulators back to the multiplier, to the ALU, and to the shifter in order to write an answer to a write bus. Without additional buses for the accumulators and for the multiplier, we would have an architectural bottleneck at the main buses. The additional buses provide increased throughput to maximize the performance of the C54x DSP.

## Slide 9
OPTIMIZED CORE
JTAG TEST/ EML CONTROL
ROM
RAM
POWER
MGMT
PROGRAM / DATA BUSES
PERIPHERAL BUS
D(15-0)
A(15-0)
PERIPHERALS
C54x Architecture
Notes: 9
The C54x has an extended set of peripherals. Let’s look at them in more detail.

## Slide 10
C54x Peripherals
HOST PORT INTERFACE (‘C542)
2 STANDARD SERIAL PORTS (‘C541)
PLL CLOCK GENERATOR
S/W WAITSTATE GENERATOR
TIMER
TDM SERIAL PORT (‘C542)
AUTO BUFFERED SERIAL PORT (‘C542)
TO BUSES
Notes: 10
The peripheral set of the C54x is quite diverse compared to many other DSPs. Onboard there's an auto-buffering serial port available on selected C54x family devices. This is essentially a serial port that links the port directly to a 2K block of memory, allowing the serial port to load memory directly without intervention from the processor which would slow the processor cycle time.
The C54x also features time division multiplexing serial ports which allow multiple C54x devices to be connected for inter-processor communication over a TDM-type of a bus structure.
Also onboard we find a timer, software wait-state generators, and phase locked loop generators. The PLL generators are offered in various styles on the C54x family. Some are fixed and have a variety of different multipliers, while others, for instance those on the C548 and the C549 devices, are actually software programmable PLLs which allow the user to throttle the device up and down at will.
In addition, there are standard serial ports and a host port interface, which allows glueless communication to a host microprocessor. This enables the microprocessor to hand off commands to the DSP without interrupting the DSP.

## Slide 11
C54x Architecture
OPTIMIZED CORE
JTAG TEST/ EML CONTROL
ROM
RAM
POWER
MGMT
PROGRAM / DATA BUSES
PERIPHERAL BUS
D(15-0)
A(15-0)
PERIPHERALS
Notes: 11
Now let’s examine the memory, power management, and test & control portions of the architecture.

## Slide 12
C54x Memory & Management
JTAG TEST/ EML CONTROL
ROM
8K X 16 PROG/ DATA (‘C541)
20K X 16 PROG (‘C541)
2K X 16 BOOT (‘C542)
PROG/ DATA RAM
5K X 16 (‘C541)
10K X 16 (‘C542)
POWER
MGMT
TO BUSES
Notes: 12
Specifically there are two different kinds of memories available on the C54x architecture, ROM and RAM. Throughout the C54x family there is a mixture of up to 48K of ROM and up to 32K of RAM depending on the specific device.
The power management features include three different idle modes or power savings modes which offer a variety of ways to control power dissipation.
The JTAG test and emulation control provides emulation ports which allow software debug using your actual physical hardware.

## Slide 13
C54x Optimized Core
TO BUSES
MAC
ALU
17 X 17 MPY
40 BIT ADDER
RND, SAT
40 BIT ALU
CMPS OPERATOR (VITERBI)
EXP ENCODER
SHIFTER
ACCUMULATORS
40 BIT BARREL
(- 16, 31)
40 BIT ACC A
40 BIT ACC B
ADDRESSING UNIT
8 AUXILIARY REGISTERS
2 ADDRESSING UNITS
Notes: 13
Now let’s return to the optimized core, and look one level deeper at the most important portions, the MAC and the ALU. We will look at the MAC first.

## Slide 14
Multiplier / Adder
DB [ 15:0 ]
CB [ 15:0 ]
PB [ 15:0 ]
A [ 39:0 ]
B [ 39:0 ]
A
B
XM YM
MPY 17 X 17
Frct / Int
Sign / Unsign
Sign / Unsign
MUX
MUX
T
FRCT
XA YA
ADDER
“0”
Detect
Round
SAT
MUX
0
OVA, OVB
ZA,ZB
Notes: 14
The multiplier adder, or MAC unit, is a very important component. In fact, it’s the main function that enables digital signal processing, since so many calculations are expressed as a “sum of products” and rely on rapid computation of these terms.

## Slide 15
Multiplier / Adder
A
B
XM YM
MPY 17 X 17
Frct / Int
Sign / Unsign
Sign / Unsign
MUX
MUX
T
FRCT
XA YA
ADDER
“0”
Detect
Round
SAT
MUX
0
OVA, OVB
ZA,ZB
DB [ 15:0 ]
CB [ 15:0 ]
PB [ 15:0 ]
A [ 39:0 ]
B [ 39:0 ]
Notes: 15
First look at the output of the multiplier. There are two accumulators. This is unique. Accumulator A and accumulator B are both 40-bit accumulators, each consisting of a 32-bit accumulator plus 8 guard bits.

## Slide 16
Two Accumulators
B
A
Notes: 16
These two accumulators facilitate many of the special features of the 54x such as the LMS instruction and the FIRS, or the symmetric FIR instruction and others.

## Slide 17
Accumulator Features
Non-pipelined multiply / add
Signed / unsigned operation
Fractional / Integer modes
2’s complement rounding
Overflow detection
32 bits saturation
A(32 : 16) input to MPY
Notes: 17
Having two accumulators is a benefit in many instances.
This enables a non-pipelined multiply and add. The MAC unit is not just a MAC unit. It's a multiplier and an adder. We can have two operands go into the multiplier and the output go to the accumulator, we can have the output of the multiplier go to the adder, or we can have operands go into the adder without going through the multiplier. So it's a non-pipeline multiply and add, which provides significant flexibility in how you use the device.
The C54x supports both signed and unsigned operations. We can have fractional and integer modes. It features 2’s complement rounding, and overflow detection. In addition, the C54x accumulators are 40 bits, which means that if overflow is detected on 32 bit results, we can correct for saturation.
Another important feature is that the A accumulator can be an input to the multiplier. These two accumulators are considered to be identical accumulators, with one difference. The output of the A accumulator is allowed to be an input to the multiplier, but an output of the B accumulator may not be an input to the multiplier.

## Slide 18
Multiplier / Adder
A
B
XM YM
MPY 17 X 17
Frct / Int
Sign / Unsign
Sign / Unsign
MUX
MUX
T
FRCT
XA YA
ADDER
“0”
Detect
Round
SAT
MUX
0
OVA, OVB
ZA,ZB
DB [ 15:0 ]
CB [ 15:0 ]
PB [ 15:0 ]
A [ 39:0 ]
B [ 39:0 ]
Notes: 18
If you look at the output of the A accumulator, it goes back to the multiplier and the adder. The output of the B accumulator can only feed back to the adder. This is useful feature. If we have an algorithm in which we want to make an assignment such as to have a coefficient times some memory value plus a memory value, and we want to add that to one of the accumulators, it begins to look like a great many operations. With this design of the multiplier/adder, we can use one data bus for one operand, and another data bus for the other operand. We can bring the coefficient in on the program bus, and perform the addition and assign that to the A accumulator. Since the A accumulator can be fed back to the multiplier, we can do this multiply and have the MAC result accumulate in the B accumulator. The point is that with two accumulators we can accumulate a sum in one accumulator, and a different sum in the other accumulator. This enables computation of two additions in the same cycle.

## Slide 19
Multiplier : 2 Buses
DB [ 15:0 ]
CB [ 15:0 ]
PB [ 15:0 ]
A [ 39:0 ]
B [ 39:0 ]
XM YM
MPY 17 X 17
Frct / Int
Sign / Unsign
Sign / Unsign
MUX
MUX
T
FRCT
Notes: 19
The bus structure of the C54x family is very flexible and works to optimize computations and increase performance. Let’s examine the way this structure is useful.
The multiplier is a fairly sophisticated device. We see in the upper left-hand corner, that there is a C bus and a D bus. This a unique feature to the C54x family, having two data buses.
If we consider a traditional algorithm such as a sum of products, we will iterate on multiplies and add them up in the accumulator. For each iteration the multiply operation can fetch both operands, one on D and one on C, feed them into the multiplier, and add them to the accumulator. The dual fetches, the multiply, and the add constitute a single cycle operation.
In certain situations, we can also use the program fetch instruction bus, as one of the operands into the multiplier.
These characteristics of the bus structure enable the designer to extract excellent performance using a C54x device.

## Slide 20
Multiplier / Adder
DB [ 15:0 ]
CB [ 15:0 ]
PB [ 15:0 ]
A [ 39:0 ]
B [ 39:0 ]
A
B
XM YM
MPY 17 X 17
Frct / Int
Sign / Unsign
Sign / Unsign
MUX
MUX
T
FRCT
XA YA
ADDER
“0”
Detect
Round
SAT
MUX
0
OVA, OVB
ZA,ZB
Notes: 20
At the bottom of this diagram, we see something called the fractional bit. If we're multiplying two fractions, for instance a Q15 number times a Q15 number, then we want to have a Q31 output, so we have to shift the output of the multiplier one position to the left.
This is a zero overhead feature of the multiplier where by setting the fraction bit in the status register, we cause the multiplier to shift the output left by one bit, producing the desired result.
We call that a fraction bit. It's fairly common to have this sort of feature on a DSP, but it's a very easy feature to implement on the C54x.
Now if we look at the output of the multiplier, we see that it feeds into the adder...

## Slide 21
Adder
0
XA YA
ADDER
“0”
Detect
Round
SAT
MUX
OVA, OVB
ZA,ZB
Notes: 21
Let’s focus on the adder section for a moment.
Since this is a non-pipelined multiply and adder, the adder can stand alone. On the left side, the input to the adder is from the multiplier. We have not shown the labels above the MUX here, but the other two inputs are the A accumulator or either of the buses, the C or D buses.
We also have, at no additional overhead, the ability to do rounding and saturation as an output of the adder, as well as setting overflow flags and zero bits.
The multiplier adder is fairly sophisticated, and it creates a lot of flexibility for the programmer.

## Slide 22
C54x Optimized Core
TO BUSES
MAC
ALU
17 X 17 MPY
40 BIT ADDER
RND, SAT
40 BIT ALU
CMPS OPERATOR (VITERBI)
EXP ENCODER
SHIFTER
ACCUMULATORS
40 BIT BARREL
(- 16, 31)
40 BIT ACC A
40 BIT ACC B
ADDRESSING UNIT
8 AUXILIARY REGISTERS
2 ADDRESSING UNITS
Notes: 22
Now let’s return to the optimized core one last time. We are ready to examine the ALU in more detail.

## Slide 23
Arithmetic Logic Unit (ALU)
OVM
C16
C
0VA, OVB, ZA, ZB
TC
A
B
DB [ 15:0 ]
CB [ 15:0 ]
A [ 39:0 ]
B [ 39:0 ]
Shifter Output [ 39:0 ]
SXM
SXM
Y
X
ALU
Notes: 23
The ALU, besides performing the standard bit manipulation and binary operations, has an adder. This gives us two adders on the C54x. In an earlier example we said we were going to accumulate a sum in the A accumulator and accumulate the result of the MAC unit in the B accumulator. This is possible because we have two adders.
The inputs to the ALU can be the two data buses (C & D buses), the feedback of the output of accumulators A & B, or the output from a shifter.
This provides a great deal of flexibility. For example, we can add a memory value to the accumulator, shifted by some amount. This seems like a simple sort of instruction. What we are asking the ALU to do is to go out on one of the data buses, the D bus, go through the shifter, shift the value in memory by 8 bits, then go to the ALU, add the shifted value to the value that's already in the accumulator and put the result back in that particular accumulator. This is an example of the type of instructions that the ALU allows us to do.
The ALU generates the standard status bits (shown in the lower right-hand corner), including overflow flags for both A and B, zero flags for both A and B, and a carry bit for both A and B.

## Slide 24
Arithmetic Logic Unit (ALU)
OVM
C16
C
0VA, OVB, ZA, ZB
TC
A
B
DB [ 15:0 ]
CB [ 15:0 ]
A [ 39:0 ]
B [ 39:0 ]
Shifter Output [ 39:0 ]
SXM
SXM
Y
X
ALU
Notes: 24
The ALU also has a C16 or carry 16 mode.
If I take a 32-bit accumulator and think of it as two 16 bit portions, where I want to treat this as a 32-bit value and add another 32-bit value to this accumulator, I would want to be sure that a one added into the 15th bit position carried to the 16th bit position, if I were doing a double wide addition operation. In order to do that, I would set the C16 bit.
If, however, I wanted to add two 16-bit values, and did not want to have this addition, I would not set the C16 bit. I would let it be equal to zero so I could have dual adds or subtracts on 16-bit values, or set the C16 bit and do single operations on 32-bit values.
Hence, we can read two 16-bit value or one 32-bit values on the two data buses, providing a big improvement in performance whenever we're doing extended precision arithmetic.

## Slide 25
ALU Features
Two 40-bit accumulators
Signed / unsigned operation
Supports 32-bit memory operands
Supports dual 16-bit operands
Overflow detection & 32-bit saturation
Supports memory to memory (PLU) operations
Notes: 25
In summary, the ALU has the following important features.
There are two 40-bit accumulators which are identical, except that the output of the A accumulator is allowed to be an input to the multiplier, but an output of the B accumulator may not be an input to the multiplier.
The device supports 32-bit memory operands or dual 16-bit operands. There is overflow detection and we can do a 32-bit saturation, which can be turned on or off, or based on a conditional operation. And finally, the ALU supports memory to memory operations.
Memory to memory operations work as follows: There is a value in memory. We’d like to compare that value in memory to a mask. We might read the value in memory into the accumulator, generate the mask, do the binary operation using the ALU, and write the value back to the accumulator, and then from the accumulator back to memory, but that's a lot of steps.
This ALU can do AND, ORs, and other binary operations directly with a value in memory in a single cycle operation, without disturbing the accumulators. This translates directly to increased performance.

## Slide 26
Features Benefits
Newest TI fixed-point DSP family
Low Power Dissipation, Low voltage operation, Idle modes, Phase- locked loop
Higher performance, lower power dissipation function
Cheaper, longer lasting batteries
Notes: 26
Let's look at some of the general features of the C54x.
One of the features that C54x has is low power and low voltage, at 3.3 volts and 2.7 volts. This allows the designer to to use less expensive batteries in most hand-held applications. For instance, in cellular phones.

## Slide 27
Features Benefits
4 internal Buses and dual address generators
Buffered Serial Ports
Enables multiple operand operations and reduces memory bottlenecks
Off-loads CPU, leaving more MIPS for additional functions
Notes: 27
The C54x has four primary internal buses, the program bus, dual input data buses, and an output write bus. This enables multiple operand operations with a single instruction, reducing the number of instructions required to complete an operation.
The C54x has a strong peripheral offering, including buffered serial ports which increase the performance of the DSP by allowing it to load the data directly into memory. This frees the processor to perform other tasks while the data is loading, and operate on the data when it is available.

## Slide 28
Features Benefits
Performance up to 100 MIPS
Large on-chip memory
Ability to provide multiple functions
Ability to adapt to changing standards and add more features
Notes: 28
Current devices include 66 MIP devices, 80 MIP devices, and a roadmap to 100 MIPS in the very near future. In addition, on chip memory sizes are getting larger as the family evolves, enabling moreoperations per device, and the ability to do increasingly complex applications like multiple channels of vocoding, in one device.

## Slide 29
Features Benefits
Host Port Interface
Thin Packaging
Glueless interface to standard 8-bit processors and TMS320 DSPs
Smaller, lighter end-equipment for lower cost
Notes: 29
The C542, C548, the C549 have a host port which looks like memory to a host device. It's a glueless interface to standard 8-bit processors as well as other TMS320 DSPs.
The TMS320C54x family takes advantage of TI’s advanced packaging technologies, enabling designers to generate smaller and lighter end-equipment devices, and to get greater density of functions in their design.

## Slide 30
C54x Software Development Tools
Notes: 30

## Slide 31
Software Development Tools
Text Editor
ASM500
LNK500
Debug
.asm
.obj
-o
.out
compile
.c
compiler shell
.lst
-L
.cmd
.map
-m
HEX500
ASM500 -LS TEST
LNK500 TEST.CMD
Notes: 31
TI offers a full suite of software development tools including code generation tools and debug verification tools. Here we see a picture of the programming flow for the current release of the code generation tools.
The code generation tools are based around the assembly. The C54x family’s main code generation tool is the assembler. We call it ASM 500. We begin by feeding source code to the assembler, which produces a relocatable object module as output. You can also have additional output such as a listing file showing your assembler source with relative addresses and op codes.
Once this object file is created, it is passed on to the to the linker. The linker's job is to assign absolute addresses to the software sections created by the assembler. It also can link in libraries and additional modules to generate a single output file called a .out file. The linker can also produce a .map file.
If, however, we want to write C code, we simply go back and put our C source into the compiler, and the output of the compiler will be a .ASM file. Now we're back where we started at the assembler, or ASM500.

## Slide 32
Debug (Verification) Tools
Target
Board
HEX500
.out
EVM500
Software Only
Contains DSP
ISA Card
XDS510
ISA card
No DSP
PC<-> Target
ROM
Prog.
SIM5XX
Debug
Notes: 32
The linker produced a output file called .out, which is an executable file that we can run on one of our software or debug verification tools. It can run on a simulator using the SIM5XX software, on the EVM500, or on a target board via an XDS510, using code generated for an EPROM programmer using our HEX500 utility.

## Slide 33
Development Environment
EPROM Programmer
S/W Simulator
C54x EVM
DSKplus
XDS510 Emulator
Object Format Converter
Object File Library
Archiver
Assembly Source
C Compiler
C Source Files
Executable COFF Object File
Linker
COFF Object Files
Assembler
Assembler Source Files
COFF Object Files
Archiver
Macro Source Files
Notes: 33
This is the whole development environment flow chart.

## Slide 34
Development Environment
EPROM Programmer
S/W Simulator
C54x EVM
DSKplus
XDS510 Emulator
Object Format Converter
Object File Library
Archiver
Assembly Source
C Compiler
C Source Files
Executable COFF Object File
Linker
COFF Object Files
Assembler
Assembler Source Files
COFF Object Files
Archiver
Macro Source Files
Notes: 34
Let's focus right in the middle, because earlier we said that the assembler was at the heart of our software development environment.

## Slide 35
Development Environment: Assembler
COFF Object Files
Assembler
Assembler Source Files
Notes: 35
What we hand to the assembler is the source file which the assembler translates into a relocatable object module. We call that a COFF file, that's a standard way of generating modular assembly language files.
Once we get the object file, the goal is to get the pieces into memory in the desired location and that's the job of the linker, which we will examine shortly.

## Slide 36
Development Environment
EPROM Programmer
S/W Simulator
C54x EVM
DSKplus
XDS510 Emulator
Object Format Converter
Object File Library
Archiver
Assembly Source
C Compiler
C Source Files
Executable COFF Object File
Linker
COFF Object Files
Assembler
Assembler Source Files
COFF Object Files
Archiver
Macro Source Files
Notes: 36
Before we look at the linker though, let’s examine the C compiler., which will also produce output the linker can operate on.

## Slide 37
Development Environment: C Compiler
Assembly Source
C Compiler
C Source Files
Notes: 37
Again, we can program in C language, and pass this C source file to the C compiler, which will generate an assembly source file.
It’s interesting and useful to note that the C54x C compiler is an optimizing C compiler. It has multiple optimization levels, which we will discuss a little bit later on. These optimization levels allow the programmer to generate more efficient code without hand-optimizing the code themselves. This saves the programmer a lot of time, and also produces very efficient code.

## Slide 38
Development Environment
EPROM Programmer
S/W Simulator
C54x EVM
DSKplus
XDS510 Emulator
Object Format Converter
Object File Library
Archiver
Assembly Source
C Compiler
C Source Files
Executable COFF Object File
Linker
COFF Object Files
Assembler
Assembler Source Files
COFF Object Files
Archiver
Macro Source Files
Notes: 38
Once we have assembly source, either hand generated, or as output from the C compiler we're back to the big picture where we're going to hand the assembly off to the assembler and the assembler is going to generate executable code.
Now we are ready to discuss the linker.

## Slide 39
Development Environment: Linker
Object File Library
Archiver
Executable COFF Object File
Linker
Notes: 39
The linker takes these object files and assigns them absolute addresses in the memory map. To this end, we have to give some instructions to the linker.
In addition to the object files we have elements from an object library that is either created by TI, such as the math library for the C compiler, or created by the developer in the case of custom functions.
The output of the linker though an executable file that can be run on any of the platforms we discussed earlier.

## Slide 40
Development Environment
EPROM Programmer
S/W Simulator
C54x EVM
DSKplus
XDS510 Emulator
Object Format Converter
Object File Library
Archiver
Assembly Source
C Compiler
C Source Files
Executable COFF Object File
Linker
COFF Object Files
Assembler
Assembler Source Files
COFF Object Files
Archiver
Macro Source Files
Notes: 40
An archiver is sometimes called the librarian.

## Slide 41
Development Environment: Archiver
COFF Object Files
Archiver
Macro Source Files
Notes: 41
The Archiver or librarian takes a collection of files and put them all in one place. It adds an index so the developer can extract one of the files from the archive, insert a new element into the archive, or retrieve an old element from the archive, modify it, and put it back.
TI’s code generation tools include several libraries or archives. For example, there is a run-time support library that comes with the C compiler, supporting several subroutines that the C compiler needs to have. An example of such a routine is the boot-up routine for initialization or start-up of a C program.

## Slide 42
Development Environment
EPROM Programmer
S/W Simulator
C54x EVM
DSKplus
XDS510 Emulator
Object Format Converter
Object File Library
Archiver
Assembly Source
C Compiler
C Source Files
Executable COFF Object File
Linker
COFF Object Files
Assembler
Assembler Source Files
COFF Object Files
Archiver
Macro Source Files
Notes: 42
Going back to our picture of the complete environment, after the linker has generated an executable file, there are several options for places to execute the code.

## Slide 43
Development Environment: Simulator
S/W Simulator
C54x
EVM
DSKplus
XDS510 Emulator
Notes: 43
The options include the software simulator, an EVM with a C54x DSP, the DSKplus demo board, or target application board using the XDS510 Emulator. These are all useful tools, each with different benefits as a testing platform.

## Slide 44
Development Environment
EPROM Programmer
S/W Simulator
C54x EVM
DSKplus
XDS510 Emulator
Object Format Converter
Object File Library
Archiver
Assembly Source
C Compiler
C Source Files
Executable COFF Object File
Linker
COFF Object Files
Assembler
Assembler Source Files
COFF Object Files
Archiver
Macro Source Files
Notes: 44
Looking one more time at the development environment, we see an object format converter.

## Slide 45
Development Environment: Object Format Converter
EPROM Programmer
Object Format Converter
Notes: 45
The object format converter is used to create a file that is compatible with an EPROM programmer. TI provides a utility with the tools called the HEX500 utility which converts an executable in TI format (a .out file from the linker) into one or more files for an EPROM programmer. This firmware can be loaded on a target platform.

## Slide 46
Linker Command File (part 1)
Example1.obj
-o example1.out
-m example1.map
MEMORY
{ Page 0 : /* Program */
PROM : org = 8000h , len = 8000h
Page 1 : /* Data */
SRAM : org = 4000h , len = 2000h
EPROM : org = 8000h , len = 2000h
}
Notes: 46
Let's focus on the linker command file to understand what it does. The linker command file is a set of instructions that tells linker where to put everything in memory. We have two main sections in the linker command file: the “memory” section, and a “sections” section.
Command line options can be run either from the command invoking the linker, or they can be placed in a batch file. Using a batch file is actually simpler and more repeatable during development, so prior to the memory section of the linker command file, you're allowed to put anything that would otherwise go on the linker command line. Here we included example1.obj, as well as some command line instructions to include this file, create an output file, and create a map file.
Next we have the memory section. Down the left side we see page zero and page one. Page zero is what the linker recognizes as program memory, and page one is what the linker understands to be data memory.
This is a Harvard architecture machine. Therefore, We can name areas in both program memory and data memory. Here, PROM is a name that the developer created. We see it’s starting address and length.We have similar syntax in page one where for SRAM and EPROM. The purpose of the memory section is to define to the linker what the hardware memory map looks like.

## Slide 47
Linker Command File (part2)
SECTIONS
{ .text :> PROM PAGE 0
.bss :> SRAM PAGE 1
.data :> EPROM PAGE 1
}
Notes: 47
The other main component of the linker command file is the “sections” section. It links the software sections to the hardware names or maps software to hardware. The .text name is a default software section name. We want the .text to go into the ROM section on page zero, which is program space. We want the .bss and the .data, both default software section names, to go into SRAM and EPROM memory space respectively.
This is the technique that we use to map software to hardware. On a more sophisticated program, this section can become more complicated. For example, there are many options. You could align a software section on a certain memory boundary, such as a 32-word boundary, or you could fill in a section of data memory with all zeros or all ones or something similar. So this can be a very sophisticated piece of the software development.

## Slide 48
C Compiler Optimization Level 0
Performs control-flow-graph simplification
Allocates variables to registers
Performs loop rotation
Eliminates dead code
Simplifies expressions and statements
Notes: 48
Now let’s return to discussion of the C compiler and the C compiler optimization levels. We can run the C compiler without any extra optimization at all, or we can request one of several optimization levels. These various levels optimize the code to make the program run faster.
Level 0 is primarily a C language improvement. It performs control-flow graph simplification and also allocates variables to registers. Rather than take a variable, make up a name, and place it in a memory location, the compiler assigns it to a register because it's accessed a lot. This improves performance.
Level 0 optimization also performs loop rotation, eliminates code that's not used or not accessed, and simplifies expressions and statements, resulting in fewer binary operations and fewer instructions.

## Slide 49
C Compiler Optimization Level 1
Performs all level 0 functions, PLUS:
Performs local copy / constant propagation
Removes local dead assignments
Eliminates local common sub-expressions
Notes: 49
The next level of optimization, level 1, does all of the level 0 optimizations plus more.
It performs constant propagation, and removes local dead assignments. It also eliminates local common sub-expressions. For instance, if there is a local subroutine that always assigns the variable Y the value of two, but never modifies Y again, that subroutine would be eliminated.

## Slide 50
C Compiler Optimization Level 2
Performs all level 1 functions, PLUS:
Performs loop optimizations
Eliminates global common sub-expressions
Eliminates global dead assignments
Performs loop unrolling
Notes: 50
Level 2 performs all level 0 and level 1 optimizations, plus more.
It does a number of loop optimizations. The algorithms associated with loop optimization are fairly complicated, and several books have been written on these techniques. However, the goal is simple enough: to make the loop as efficient as possible.
In level 1 optimization, local common sub-expressions and dead assignments were eliminated. Now we're going to eliminate similar things globally in Level 2 optimization.
Finally, one of the most important optimizations in level two is loop unrolling. Consider a loop that's not very long, two or three iterations. By simply rewriting that code two or three times, all of the overhead associated with initializing the loop could be eliminated. If the loop was 1,000 iterations, it would probably be inefficient to unroll that loop. But if the loop was short, we could improve the efficiency of the code. We would increase the code size slightly, but the program would run faster.

## Slide 51
C Compiler Optimization Level 3
Performs all level 2 features, PLUS:
Removes all uncalled functions
Simplifies functions that have unused return values
Expands calls to small functions inline
Identifies file-level variable characteristics
Notes: 51
Level 3 optimization performs all the optimizations of levels 0, 1, and 2 plus more, focusing on subroutines and calls.
Uncalled functions are removed, and functions with unused return values are simplified. For instance, if you have a function that you've compiled and linked, it's part of the code. If it's never called, the optimizer will discard it reducing the code size.
If we have a short function such as one which takes absolute value of a number, rather than call a subroutine, utilize the stack, and add the overhead associated with a subroutine call, this optimization will simply make that function an in-line set of statements. This eliminates the overhead associated with the subroutine. If this is done a lot, code size would increase noticeably, so there are always tradeoffs depending on the particular desired characteristics of the final program, but the optimizations can substantially improve performance.

## Slide 52
C Compiler Optimization
Shortens development time
Eliminates the need for hand benchmarking
Produces more efficient code
Simplifies convergence on the best speed / code size solution.
Notes: 52
Optimization shortens the amount of time it takes for a code developer to optimize their code. It eliminates the need for hand benchmarking and converges on the best set of code. It is particularly useful if you're using arrays. Arrays are easy to understand and to write the code for, but they're less efficient than implementing the arrays as pointers in C. The optimizer will do that for you, saving a lot of time, and producing a better result.
We have multiple levels of optimization because as you do more and more optimization, you tend to increase the size of the code and sometimes it just won't fit in memory. So the developer has to study their particular application and usually through experimentation, identify the level of optimization that produces the code with the optimal size and speed combination for their specific application.

## Slide 53
TMS320C54x Programming
ANSI C compiler :
  Architecture for code efficiency
Assembler :
  Mnemonic or Algebraic Syntax
Notes: 53
TI's C compiler is an ANSI C compiler. This means it complies with the ANSI standard including a floating-point library.
There are also ways to utilize the C54x as a floating-point device. When you do floating-point, you must manage the exponent and mantissa, so the C compiler includes a floating-point math library.
The assembler offers two syntax styles, a mnemonic assembler and an algebraic assembler.

## Slide 54
Mnemonic Syntax
ABS A,B
ADD #512,3,A
FRAME 26
MAC Table1, B
POPM AL
Notes: 54
Let's look at what the differences are between Mnemonic and Algebraic syntax, using five instructions as an example.
The mnemonic assembler might be called a traditional assembler. In the mnemonic syntax, to take the absolute value of the number that's in accumulator A and place the result in accumulator B, we use the ABS instruction and then over to the right we have the operands A and B.
In the second instruction, we are adding a number, 512, shifted to the left by three places using the shifter, and placing the result in accumulator A.
The third example shows how to move the stack pointer by 26 memory locations. We simply say frame 26. In C language, when we do a subroutine call we have to allocate space on the stack for the local variables. That space on the stack is considered to be a frame, so we say we want to have a frame of 26 words.
The fourth instruction, MAC, says multiply and accumulate the value pointed to by table one, multiply that value times the value in the T register (implied), and place the product in the B accumulator.
Finally, we pop the lower half of the accumulator off the stack and place it back in the accumulator. Now let’s see what the same instructions look like using algebraic syntax.

## Slide 55
Algebraic Syntax
B = | A |
A = A+#512<<3 OR A+ = #512<<3
SP = SP + 26
B = B + T*Table1
AL = pop( )
Notes: 55
Algebraic assembly expresses the instructions as equations.
In the first expression, we take the absolute value of the number in A, and assign it to B. In the second, we'll take the number 512, shift it to the left by three, add it to A and place the result back in A. The third instruction our frame instruction where we want to increase the frame by 26 words, that is, increase the stack pointer by 26 words. The fourth instruction multiplies the value pointed to by table one by the value in the T register and then adds the value in B and accumulates the result in B. Finally, we want to pop a value off the stack and place it in the accumulator.
This dual syntax raises the question of whether the assemblers differ a lot. They're clearly a different style, but they both generate exactly the same op codes. These are isomorphic tools. Which assembler to use really becomes a matter of personal taste. It simply makes it easier to program the device for developers who have a preference for a particular style, or history programming a device which only uses mnemonic or algebraic syntax.

## Slide 56
Example System
C 54x
PROM
code
SRAM
var
EPROM
const
Program Memory
Data Memory
8000
FFFF
4000
6000
8000
A000
Notes: 56
Here we see a hypothetical system containing a C54x, some elements of program memory, and some elements of data memory. Let’s examine how it relates to linker command files.
Specifically look at where the code is. It's located at address 8,000 in program memory. Note the EPROM in data memory. It's also located at address 8,000, but in data memory, not program memory. If you look at the associated linker command file in the next slide we'll focus on those two elements.

## Slide 57
Example Linker Command File
Vectors.obj
-o myfile.out
-m myfile.map
MEMORY {
PAGE 0: EPROM: org = 0E000h len = 01F80h
VECS: org = 0FF80h len = 00080h
PAGE 1: SPRAM: org = 00060h len = 00020h
DARAM: org = 00080h len = 01380h
DEPROM: org = 08000h len = 08000h }
SECTIONS {
.vectors : > VECS PAGE 0
.text : > EPROM PAGE 1
.data : > DEPROM PAGE 1
.bss : > SPRAM PAGE 1 }
Notes: 57
The code, which is located in the .text section was at 8,000 in program memory, and the dot data section is going to be in the EPROM at address 8,000. Someone may point out that we shouldn't be putting .data section in EPROM, and that's probably true, but we have done so in this example to demonstrate the possibility.
Now suppose we didn't want the .data section to go into the DEPROM. Suppose I wanted it to go in SRAM. Then next to the.data section, I would replace the DEPROM reference with an SRAM reference and the linker would put it in the new desired location.
In the memory section, let's find the code. It is actually down in the bottom. It's called .text. We’re going to put that, in the middle of the “sections” section in EPROM, and note that the memory section says EMPROM starts at address 8,000 and it has a particular length (01F80h).
We can also look down at the bottom for the .data section in “sections”, where the data section appears in the memory section called DEPROM. If we look back up in the memory section to understand the hardware section, we see its DEPROM, originating at 08000h with length 08000h.

## Slide 58
TMS32054x Simulator
DOS or Windows PC versions
Unix versions available
State accurate simulation
Notes: 58
This section discusses the debug tools specifically, and first focuses on the simulator. The simulator is available both in DOS and in UNIX versions. The DOS version can be invoked from a DOS window or as a Windows PC program as well. The UNIX versions look a lot like the PC Windows versions.
It's important to note that this is a state accurate simulator. This means it has been built from the same database that the devices have been built from. So when simulating a device, its exactly as if it were real hardware. When you take code written for the simulator and move it to a target board, it operates exactly the same way.

## Slide 59
DSKplus Board Block Diagram
Analog Input
Analog Output
10MHz CLK
14- Pin XDS
Port
Parallel Port Interface Logic
Expansion Interface
Analog Interface ‘AC01
PLL
TDM
XDS
INTs
HPI
BSP
Addr
Data
Control
External Memory I/F
10KWords DARAM
‘C542
Notes: 59
The DSKplus is a small demonstration board which has a DSP on it, in this case the 542. It has an A/D and D/A, one of the TI AIC, with an analog in and analog out so speakers, radios, tape players, CD players, etc., can be input into the DSP. It also has an external power source and a connector at the interface to the PC. There is a parallel interface port shown on the right side of this diagram. This port connects to the printer port on a PC. At the bottom of the block diagram we also see an expansion interface.
All of the pins from the DSP are brought out to this expansion interface so that headers can be added to have additional memory, or test points, or to connect a different A/D and wire that in to either I/O space or a serial port. Additionally, the connectors enable attachment of a header in order to use a JTAG interface to this board, making the DSKplus a target board as well as a stand-alone board.
All of these features combine to make the board very flexible.

## Slide 60
TMS320C54x DSKplus
Standalone board with parallel printer port connection
40 MIPS TMS320C542
  10K words of on-chip RAM
Voice quality analog interface to line I/O or speaker /microphone with 320AC01 AIC
Windows debug with GO DSPs Code Explorer
Notes: 60
The DSKplus is a stand-alone board. It requires an external power source. It's 40 MIPS, 542 onboard, 10K of RAM, and it has a debugger with a graphic interface, called Code Explorer built by Go DSP, a third party. Code explorer is a graphic interface that comes with the DSKplus.

## Slide 61
TMS320C54x DSKplus
Algebraic assembler, applications & demo software included
All signals brought out to board periphery
Universal, regulated power supply & cable included
Embedded emulation support via JTAG
Above plus documentation for $149 !
Notes: 61
Also, the DSKplus uses the algebraic assembler. There are a number of applications that come with this board and a lot of demo software.
All the signals are brought out to the expansion interface. It comes with a power supply. Embedded emulation is supported via JTAG enabling use of the DSKplus as a target board.

## Slide 62
DSKplus System Requirements
Starter Kit
Parallel Printer Port Cable
:
25 pin to 25 pin adapter
5VDC power supply
Computer
IBM PC Compatible
DOS 4.01 or later
DSK User’s Guide
Notes: 62
The DSKplus starter kit includes the board, software tools and of course, a user's manual that explains how it works. It also includes a parallel printer port cable to interface to a PC, and a power supply.

## Slide 63
Connecting the DSKplus to your PC
Install DSKplus software
Connect the DB25 cable to the PC’s parallel port
Connect the DB25 cable to the DSKplus board
Connect the power cable 5.5mm plug into the power jack on the DSKplus board
Notes: 63
To connect the DSKplus, simply install the software, connect the parallel cable to the DSKplus parallel port, connect the other end of the cable to your PC, connect the power, and you are ready to begin running programs.

## Slide 64
Connecting the DSKplus to your PC
9VAC Adapter
Notes: 64
Connecting the DSKplus takes only a matter of seconds. Other devices such as speakers, microphones, or tape recorders can also be connected to the system. The DSKplus sells for only $149 and may be purchased for $99 through Oct 31, 1997 with a coupon included with the C54x computer based training CD.

## Slide 65
XDS510
PC plug-in card or
Unix-based workstation version
Scan-based emulator
Test Bus Controller (TBC)
User interface like other tools
Debug actual target
Notes: 65
Now let’s investigate emulation. The XDS510 emulator is available as a plug in card for PC’s or as a standalone desktop unit for UNIX based workstations. With this system, customers can load programs and debug their target board.
The XDS510 is a serial scan path based emulator, as opposed to the old fashioned ICE (in-circuit emulators) that are used in lower speed processors. It contains a test bus controller - a device that acts as an interface between the debugging platform and the DSP or DSPs. You can have multiple DSPs in your scan path. The user interface of the CDS510 looks very much like the simulator ( and other tools) , but with some additional drop down menus for hardware breakpoints. To use the XDS510, a debugger interface is attached to the DSP. At one end it connects to a SCSI port on the host machine, on the other end it plugs into the target board.
Similar products are also available from a variety of third parties.

## Slide 66
TMS320C54x EVM Board
Traditional EVM PC Board
40 MIPS based on TMS320C541
128K words of zero wait-state RAM
Voice quality analog interface to line I/O or speaker / microphone with 320AC01 AIC
External serial port connector
Two bi-directional PC hose communication channels
Notes: 66
The EVM is a traditional PC add-in ISA-bus card, rather than an external card like the DSKplus which sits out on the table and requires an external power source.
Like the DSKplus, the EVM has a DSP, an AIC, a test bus controller, analog inputs and outputs, and additional memory. Somewhat different from the DSKplus, the EVM has a serial connector so that if someone didn’t want to use the AIC on this board, but a different A/D with higher resolution or faster speeds, the external board could be connected to the serial port.
It has a C541 on it. Even if a customer is using a different C54x device, they could still debug with this board. It can be used in the same portion of the development cycle as the simulator to write & test code, but allows the developer to run on actual DSP hardware rather than the simulator.
The EVM has 128K words of zero wait-state SRAM which provides and excellent environment for loading and running larger programs than one might run on a DSKplus.

## Slide 67
Summary
C54x is a high performance architecture with unique features
TI offers full suite of software development tools
TI and 3rd parties offer full range of hardware development tools
Assembler is available in 2 forms
DSKplus is a special product available at low cost
Notes: 67
The C54x is a high performance architecture with several unique features, a lot of improved peripherals over previous families, and a lot of performance and memory improvements as well.
TI offers a full suite of software and hardware development. There is a software simulator for testing and debugging code, an EVM for running code or parts of our algorithm on an actual DSP, the XDS510s in both PC and UNIX workstation varieties, and the DSKplus , which is a low-cost entry into the hardware debugging environment. There are also several third parties that offer a multitude of hardware and software development tools.
The assembler is available in two forms, both in algebraic and a mnemonic format, also on both UNIX platforms and PC platforms.