## Slide 1
TMS320C6x Architecture and Software Development Tools
Notes: 1
Welcome to the C6x tools demo module. By understanding the unique intertwined nature of the C6x architecture and code generation and debugging tools, you will be able to maximize the performance of your DSP designs and complete them in shorter periods of time with significantly reduced effort. This capability is enabled not only by the C6x product, but by the tools helping you to achieve the full capacity of the TMS320C6x Digital Signal Processor.

## Slide 2
Module Overview
Benchmarks
Functional view of C6x architecture using code example
Optimization & code generation tools
Notes: 2
Our journey into the C6x tools begins with a brief look at C6x benchmarks on some common DSP algorithms. Next we will delve into the architecture of the C6x to begin to understand what makes this such a unique DSP. With the architectural components as a knowledge base, we will explore a variety of coding methods and code generation tools designed to make the C6x the easiest TI DSP to program.

## Slide 3
C62xx C5x
Complex Block FIR 1,292 3,692
16 taps, 40 outputs
LMS Adaptive FIR 44 95
16 taps, 1 output
IIR 27 93
256 Point FFT 4,168 20,907
Benchmarks in Clock Cycles
Notes: 3
To provide a frame of reference for benchmarking, the C62xx is compared to another popular TI DSP family, the C5x DSP.
We chose four algorithms to examine: a complex block finite impulse response (or FIR) filter, a least mean square (or LMS) adaptive FIR filter, an infinite impulse response (or IIR) filter, and a 256-point Fast Fourier Transform (or FFT). These benchmarks are all mathematically intensive algorithms that are commonly found in DSP applications.
For the complex block FIR with 16 taps and 40 outputs, it takes 1,292 clock cycles on the C6x while on the C5x is takes nearly three times as many at 3,692 clock cycles. The LMS adaptive FIR, with 16 taps and one output takes 44 clock cycles on the C6x, and it takes 95 cycles, or more than twice as many, on a C5x. Examining an IIR filter, it takes 27 clock cycles on a C6x and 93, or about three and a half times as many on a C5x. And finally, the 256-point FFT takes 4,168 clock cycles on the C6x and nearly 20,907 on the C5x, or about one fifth as many cycles using a C6x.

## Slide 4
C62xx C5x
DSP Cycle Time 5 ns 20 ns
Complex Block FIR 6.46 us 73.84 us
16 taps, 40 outputs
LMS Adaptive FIR 220 ns 1900 ns
16 taps, 1 output
IIR 135 ns 1860 ns
256 Point FFT 20.84 us 418.14 us
Benchmarks in Time
Notes: 4
Because the processor cycle time for the C6x is 5 nanoseconds and the processor cycle time for the C5x is 20 nanoseconds, we see an even more dramatic shift when we look at benchmarks in terms of time.
For instance, the last benchmark shown, the 256-point FFT, takes 418.14 microseconds for a C5x DSP, while the C6x completes it’s task in 20.84 microseconds, or twenty times faster.

## Slide 5
Most DSP algorithms can be expressed as :
Sum of Products
N
an xn
n = 1
Y =
*
Notes: 5
These algorithms are similar to each other, and to other typical DSP algorithms, in that they can be expressed as a sum of products.
For example, as Y equals the summation for n equals one to some number N, of An times X n. Let’s use this example to build the C6x architectural components.

## Slide 6
Example - Multiply
Y =
40
An Xn
n = 1
*
MPY A, X, A*X
.?
Notes: 6
The first instruction needed to do the sum of products is a multiplication. We multiply A with X and place the result in A times X.

## Slide 7
Example - Multiply .M Unit
Y =
40
An Xn
n = 1
*
MPY A, X, A*X
.M
Notes: 7
This function requires a hardware multiplier. Thus the C6x incorporates a 16 by 16 multiplier, represented by the notation .M.

## Slide 8
Example - Add
Y =
40
An Xn
n = 1
*
MPY A, X, A*X
ADD A*X, Y, Y
.M
.?
Notes: 8
The second function needed to create the sum of products, is addition. We add the product “A times X” with Y, creating a running sum in Y.

## Slide 9
Example - Add .L Unit
Y =
40
An Xn
n = 1
*
MPY A, X, A*X
ADD A*X, Y, Y
.M
.L
Notes: 9
The addition requires a hardware adder, which is designated as the .L unit. This notation illustrates that this functional unit not only performs addition, but also other traditional ALU functions including subtraction, logical ANDs, ORs, and Exclusive-ORs.
Later we will see that the notation you might have expected, “A” is used elsewhere in the architecture.

## Slide 10
Example - Add
Y =
40
An Xn
n = 1
*
MPY A, X, A*X
ADD A*X, Y, Y
.M
.L
A
X
A*X
Y
?
Notes: 10
The terms in our sum of products equation, A, X, A times X, and Y, are stored in...

## Slide 11
Example - Register File
Y =
40
An Xn
n = 1
*
MPY A, X, A*X
ADD A*X, Y, Y
.M
.L
A
X
A*X
Y
Sixteen 32-bit Registers
Register File
Notes: 11
a register file consisting of sixteen 32-bit registers.

## Slide 12
LDH *MemA,A
LDH *MemX,X
MPY A, X, A*X
ADD A*X, Y, Y
STH Y,*MemY
Data Memory
Example - Load/Store
Y =
40
An Xn
n = 1
*
.M
.L
A
X
A*X
Y
Sixteen 32-bit Registers
Register File
.?
Notes: 12
The values in the registers and are transferred from data memory using LOAD instructions. To move values from the register file back into data memory, a STORE instruction is used.
In this example, we use LDH, or Load half word, to load the 16 bit values. Somewhere in data memory, there exists a value that we want to obtain and put into register A. We refer to that value as *MemA, so we we load H, *MemA, and put that into register A, and load H, *MemX and place that in register B.
Once the values exist in the registers A and X, we multiply them together, placing the value in A times X, and we update the running sum Y by adding A times X to Y and placing the result in Y.
And finally, we use a store instruction, in this case a store half word, to store the running sum Y back into data memory.
We add a functional unit to the architecture, shown here in green, to get values to and from data memory and to and from the register file.

## Slide 13
LDH *MemA,A
LDH *MemX,X
MPY A, X, A*X
ADD A*X, Y, Y
STH Y,*MemY
Data Memory
Example - Load/Store .D Unit
Y =
40
An Xn
n = 1
*
.M
.L
A
X
A*X
Y
Sixteen 32-bit Registers
Register File
.D
Notes: 13
This new functional unit is designated the .D unit, or data mover.

## Slide 14
Three load instructions exist:
  LDW Load 32-bit word
  LDH Load 16-bit half-word (short)
  LDB Load 8-bit byte
Allow signed or unsigned loads. e.g. LDHU
CPU supports three store instructions: STW, STH, STB
Load Instructions
Notes: 14
In our example we have used the LDH or LoadHalf Word instruction. However, the C6x architecture is a native 32-bit machine, and is also byte addressable. There are three different load instructions available on the C6x, the LDW or Load Word, the LDH or Load Half Word, and the LDB or Load Byte instruction.
We can also allow for either signed loads or unsigned loads with slight modification to the instruction syntax. We're loading data and in a two's complement number system, so the leading bit or the most significant bit also contains sign information. For a negative number, that sign bit is one. In order to bring it into a register that's 32 bits, we must be able to sign extend to indicate a negative value.
The CPU also supports three store instructions and they are STW, or store word, for 32-bit values, store H for 16-bit values, and store byte for 8-bit values.

## Slide 15
LDH .D *MemA,A
LDH .D *MemX,X
MPY .M A, X, A*X
ADD .L A*X, Y, Y
STH .D Y,*MemY
Data Memory
.M
.L
A
X
A*X
Y
Sixteen 32-bit Registers
Register File
.D
Notes: 15
Now let’s go back and to our code example and put the functional units by the instructions that are performing the instruction. LDH is done by the .D unit, multiply uses the .M unit, and add uses the .L unit.
From a programming point of view, its easy to see that for more complicated code it would quickly become difficult to keep track of assigning all the functional units to the instructions. In reality, the programmer doesn't have to worry about this task at all. The development tools will automatically do it for them. But, for the sake of this example, to illustrate the functional units and their associated instructions, we will include this coding step.

## Slide 16
LDH .D *MemA,A
LDH .D *MemX,X
MPY .M A, X, A*X
ADD .L A*X, Y, Y
STH .D Y,*MemY
32-bits
Data Memory
.M
.L
Register File A
.D
A0 A
A1 X
A2
A3 A*X
A4 Y
•
•
•
A15
Notes: 16
Let’s examine the register file. This register file is designated “Register File A”.

## Slide 17
LDH .D *MemA,A0
LDH .D *MemX,A1
MPY .M A0, A1, A3
ADD .L A3, A4, A4
STH .D A4,*MemY
32-bits
Data Memory
.M
.L
Register File A
.D
A0 A
A1 X
A2
A3 A*X
A4 Y
•
•
•
A15
Notes: 17
It contains 16 32-bit values, A0 through A15, and for our example we have placed A in register A0, X in register A1, A times X in register A3, and Y in register A4.
And now, in the code we're going to substitute the register names (A0, A1, etc) for the A, X, A times X, and Y notations we used before.

## Slide 18
LDH .D *MemA,A0
LDH .D *MemX,A1
MPY .M A0, A1, A3
ADD .L A3, A4, A4
STH .D A4,*MemY
32-bits
Data Memory
.M
.L
Register File A
.D
A0 A
A1 X
A2
A3 A*X
A4 Y
•
•
•
A15
Notes: 18
We said before that this example was a sum of products. Right now we're just doing this loop one time. In order to complete the sum of products, we’ll need to execute this code 40 times, so we add a loop.
One method to complete the task would be to literally copy the 4 loop instructions 40 times and then finish with the store instruction, but this method would result in very large code size.
A better method would be to take this section of code and put it into a loop and execute the loop 40 times.

## Slide 19
1. Add branch instruction (B) and a label
2. Create a loop counter with proper value
3. Add an instruction to decrement the loop counter
4. Make the branch conditional based on the value in the loop counter
Creating a Loop
Notes: 19
There are four steps to create a loop.
First, we add a branch instruction and a label. Then a loop counter is created with the proper value. Third an instruction is added to decrement the loop counter within the loop itself. The final step is to make the branch conditional based on the value in the loop counter.

## Slide 20
A0 A
A1 X
A2
A3 A*X
A4 Y
A15
LDH .D *MemA, A0
LDH .D *MemX, A1
MPY .M A0, A1, A3
ADD .L A3, A4, A4
B .? loop
STH .D A4, *MemY
32-bits
Data Memory
.M
.L
Register File A
.D
.?
loop:
.
.
.
1
Notes: 20
Let’s implement step one, adding the branch instruction and label.
What functional unit would be used to implement the branch?

## Slide 21
A0 A
A1 X
A2
A3 A*X
A4 Y
A15
LDH .D *MemA, A0
LDH .D *MemX, A1
MPY .M A0, A1, A3
ADD .L A3, A4, A4
B .S loop
STH .D A4, *MemY
32-bits
Data Memory
.M
.L
Register File A
.D
.S
loop:
.
.
.
1
Notes: 21
The unit is a .S unit, or a shifter. It does shifts as well as branches. The notation .B, which seems like a likely name, is being used for something for in this system as we will see later.
This multiple functionality of the architectural units is quite useful, and in fact there are several functional units which can perform a variety of tasks. The .S unit not only does branches and shifts, but can also do addition and subtraction, and can be used to load constants. The .M unit is just a multiplier. The .L unit is an ALU, and does addition, subtraction, and logicals such as AND, OR and Exclusive Or. And, although the .D unit’s primary function is to loads and stores in memory, it also has the capability to do adds and subtracts.
This functional unit flexibility allows the compiler to do a much better job since it has choices regarding which units to use to execute a particular task.

## Slide 22
MVK - move a 16-bit Konstant into a register
MVK .S 40,A2 ;A2 = 40
2
Notes: 22
The second step in creating the loop is to create a loop counter with the correct value. To create a loop counter and initialize it with a value, we're going to use a move K instruction, or a move a 16-bit constant into a register.
We move the constant 40 into register A2 using the .S unit.
move K takes a 16-bit value and puts it into the lower 16-bits of a register. Later we will see a similar instruction, “Move KH” which will take a 16-bit constant and put it into the upper half of the 32-bit register.

## Slide 23
A0 A
A1 X
A2 count=40
A3 A*X
A4 Y
A15
MVK .S 40, A2
LDH .D *MemA, A0
LDH .D *MemX, A1
MPY .M A0, A1, A3
ADD .L A3, A4, A4
B .S loop
STH .D A4, *MemY
32-bits
Data Memory
.M
.L
Register File A
.D
.S
loop:
.
.
.
2
Notes: 23
Returning to our code example, we insert the move K instruction, which initializes the loop counter, A2.

## Slide 24
A0 A
A1 X
A2 count=40
A3 A*X
A4 Y
A15
MVK .S 40, A2
LDH .D *MemA, A0
LDH .D *MemX, A1
MPY .M A0, A1, A3
ADD .L A3, A4, A4
? ? ?
B .S loop
STH .D A4, *MemY
32-bits
Data Memory
.M
.L
Register File A
.D
.S
loop:
.
.
.
3
Notes: 24
The third step is to decrement the loop counter just before we exit the loop.

## Slide 25
A0 A
A1 X
A2 count=40
A3 A*X
A4 Y
A15
MVK .S 40, A2
LDH .D *MemA, A0
LDH .D *MemX, A1
MPY .M A0, A1, A3
ADD .L A3, A4, A4
SUB .L A2, 1, A2
B .S loop
STH .D A4, *MemY
32-bits
Data Memory
.M
.L
Register File A
.D
.S
loop:
.
.
.
3
Notes: 25
The correct instruction is subtract, .L, A2, one, A2. This subtracts one from the value of the contents of register A2, and places the result back in A2.

## Slide 26
All instructions are conditional based on zero or nonzero values in:
A1, A2, B0, B1, B2
Code Syntax
[A2]
[!A2]
Execute instruction if :
A2 = 0
A2 = 0
[condition] B .S loop
4
Notes: 26
The fourth step in creating the loop is to make that branch conditional.
All instructions on the C6x are conditional. So not only branches, but the add we saw, the multiply, the loads, the stores, every instruction on the C6x is conditional. The conditions are based on zero or non-zero values in the registers, A1, A2, B0, B1, and B2.
The syntax showing A2 in brackets indicates an instruction is to be executed as long as A2 is not equal to zero.
If an exclamation point is added in front of the A2, meaning NOT A2, this indicates the instruction is to be executed if A2 is equal to zero.

## Slide 27
A0 A
A1 X
A2 count=40
A3 A*X
A4 Y
A15
MVK .S 40, A2
LDH .D *MemA, A0
LDH .D *MemX, A1
MPY .M A0, A1, A3
ADD .L A3, A4, A4
SUB .L A2, 1, A2
B .S loop
STH .D A4, *MemY
32-bits
Data Memory
.M
.L
Register File A
.D
.S
loop:
[A2]
.
.
.
4
Notes: 27
Returning to our code example, we wanted to make the branch conditional based on A2, so we put in A2 in brackets at the end of the loop, indicating we will continue to execute the loop until A2 is equal to zero.
We will execute this loops 40 times, then fall out of the loop when A2 is equal to zero, and store the final result which is in register A4 to memory using *MemY.

## Slide 28
A0 A[ . . . ]
A1 X[ . . . ]
A2 count=40
A3 A*X
A4 Y
A15
MVK .S 40, A2
LDH .D *MemA, A0
LDH .D *MemX, A1
MPY .M A0, A1, A3
ADD .L A3, A4, A4
SUB .L A2, 1, A2
B .S loop
STH .D A4, *MemY
32-bits
Data Memory
.M
.L
Register File A
.D
.S
loop:
[A2]
A X Y
*
.
.
.
Notes: 28
Now let's revisit how we get values to and from memory.
An and Xn are actually arrays of 40 values that we're multiplying. So we need some way of accessing the data in the arrays and we do this by using pointers.
The *(*) notation means we are using pointers. To use a pointer we initialize it to point to the first memory location in the array.

## Slide 29
Using Pointers
Loading a pointer:
MVK .S A, A5
MVKH .S A, A5
Using a pointer:
LD .D *A5++, A0
&A
A5
A(0)
A(1)
A(2)
A(3)
+ +
. . .
Notes: 29
To perform the initialization, the move K or move KH instructions are used.
To load a pointer or to initialize it to some value, the instruction move K, .S, A, A5 is used. This instruction finds A in the memory map, and loads the lower 16 bits of that address into register A5.
Then, using the move KH, wherever A is in the memory map, the upper 16 bits of that address is placed into the high half, or upper 16- bits, of register A5.
When we have executed these two instructions, register A5 contains the address of A and it points to the first location in the A array, or A0.

## Slide 30
Code changes -- replace:
MemA *A5++
MemX *A6++
MemY *A7
Using Pointers
Notes: 30
As we travel through the code, we need to increment the pointer each time we need the next value in the array. To increment the pointer, the”++” notation is used.

## Slide 31
A0 A
A1 X
A2 count=40
A3 A*X
A4 Y
A5 &A(n)
A6 &X(n)
A7 &Y
:
A15
MVK .S 40, A2
LDH .D *A5++, A0
LDH .D *A6++, A1
MPY .M A0, A1, A3
ADD .L A3, A4, A4
SUB .L A2, 1, A2
B .S loop
STH .D A4, *A7
32-bits
Data Memory
.M
.L
Register File A
.D
.S
loop:
[A2]
Notes: 31
Now lets return the code example with the substitutions made. *MemA now is *A5++. *MemX is now *A6++, and *MemY is now *A7.
So we do a load, .D, *A5++ into register A0. This takes the value pointed to by A5 and places it into register A0. Then we increment the pointer, moving to the next place in memory.

## Slide 32
A0
A1
A2
A3
A4
A15
32-bits
Data Memory
.M1
.L1
Register File A
.D1
.S1
.
.
.
B0
B1
B2
B3
B4
B15
32-bits
Register File B
.
.
.
.M2
.L2
.D2
.S2
Notes: 32
At this point, we want to introduce an important fact. There's another duplicate half to the C6x architecture, which includes another shifter, another multiplier, another ALU, another D unit, and another 16 by 32-bit register file, the B register file. This “other half “ doubles the performance capability of the architecture we have built so far.

## Slide 33
Code Review (using side A only)
MVK .S1 40, A2 ; A2 = 40, loop count
loop: LD .D1 *A5++, A0 ; A0 = A(n)
LD .D1 *A6++, A1 ; A1 = X(n)
MPY .M1 A0, A1, A3 ; A3 = A(n) * X(n)
ADD .L1 A3, A4, A4 ; Y = Y + A3
SUB .L1 A2, 1, A2 ; decrement loop count
[A2] B .S1 loop ; if A2 < > 0, branch
ST .D1 A4, *A7 ; *A7 = Y
Notes: 33
This slide shows the commented completed code example we have built.

## Slide 34
ISC
MPY
LD
B
Single Cycle
Multiply
Load
Branch
37
5
1
4
0
1
4
5
Type Description # Instr. Delay
‘C62xx Instruction Types and Execution Cycles
Notes: 34
Another important concept that we need to discuss is the amount of time it takes to actually execute instructions. All instructions execute in one cycle, but some have delay associated with availability of the result.
The multiply instruction has a one-cycle delay. When we multiply A0 and A1 together, the result is not available in that clock cycle. It appears in register A3 in the following clock cycle. We are still able to execute another multiply in the next clock cycle, so the functional unit capabilities are not wasted waiting on the result. However, the result is delayed until the following clock cycle for the multiply.
Most instructions don't have any delay . But the multiply, the load, and the branch have one, four, and five delay cycles associated with their results.
To understand what is occurring during this delay time, consider that during a load, data is being transferred from memory. Thus, the address of the location being read must be generated and sent to memory, there is a waiting period for the data value to come back, then the data value is read, and finally written into the register. These transactions take time, but the functional unit is not tied up for that amount of time. The instruction executes in one cycle, and only the result is delayed.

## Slide 35
Instruction Types #NOPs
ISC
MPY
LD
B
Single Cycle
Multiply
Load
Branch
0
1
4
5
0
1
4
5
Type Description Delay Slots #NOPs
Notes: 35
We have a dilemma now because our example code is not going to work. We have a multiplied A0 and A1 and we're putting the result into A3, and then we want to add A3 to A4. But the result will not be seen in A3 until the following clock cycle. In order to get this code to work, we introduce an instruction called the NOP of “no operation”. This instruction is used to fill the delay slots.

## Slide 36
MVK .S1 40, A2
loop: LDH .D1 *A5++, A0
LDH .D1 *A6++, A1
NOP
NOP
NOP
NOP
MPY .M1 A0, A1, A3
NOP
ADD .L1 A3, A4, A4
SUB .L1 A2, 1, A2
[A2] B .S1 loop
NOP
NOP
NOP
NOP
NOP
STH .D1 A4, *A7
Notes: 36
For the multiply, if there is a data dependency like the one in our example code, one NOP is placed after the instruction. For a load, four NOPs are added, and for the branch, five NOPs are inserted.
There are issues to consider when using NOPs however, and one is code size. To avoid using multiple instructions for multiple NOP commands, a numerical argument is added.

## Slide 37
MVK .S1 40,A2
loop: LDH .D1 *A5++,A0
LDH .D1 *A6++,A1
NOP 4
MPY .M1 A0,A1,A3
NOP
ADD .L1 A3,A4,A4
SUB .L1 A2,1,A2
[A2] B .S1 loop
NOP 5
STH .D1 A4,*A7
Notes: 37
We are finally ready to benchmark our code example.
The first load instruction takes one cycle, as does the second load. We add four delay cycles for the NOPs, a total of six. Adding the multiply and its associated NOP brings the total to eight. The add and subtract increase the total to ten. The branch plus the delay slots bring the total to 16. We're going to do this loop 40 times, so the amount of time it's going to take to do this is 16 times 40, or 640 cycles, the way the code is now written.
DSP aficionado's joke that the NOP command stands for “not optimized properly”. In other words, when inserting all of these delay cycles, we are not getting the maximum performance from the part. In fact, once this code is properly optimized, we will see that it is possible to reduce the benchmark to 28 clock cycles.
To accomplish this amazing performance improvement, we will use the powerful optimization capabilities of the C6x development tools.

## Slide 38
How can we improve performance of our algorithm?
Fill delay slots with useful instructions - replace NOPs
Use instructions in parallel
Notes: 38
To begin the optimization, we could replace the NOP delays with useful instructions Another possibility is to execute instructions in parallel.

## Slide 39
32 bits
Instruction
256 Bits
I1
I2
I3
I4
I5
I6
I7
I8
Fetch Packet (8 x 32-bit)
VLIW
I 1
I 2
I 3
I 4
I 5
I 6
I 7
I 8
Advanced VLIW - VelociTITM
Notes: 39
TI's advanced VLIW architecture, or VelociTI takes eight 32-bit instructions, and creates a fetch packet., using a VLIW, or very long instruction word, of 256 bits.

## Slide 40
Code Example
B .S1
| | MVK .S2
ADD .L1
| | ADD .L2
| | MPY .M1
MPY .M2
| | LD .D1
| | LD .D2
Notes: 40
Recall that we just said a fetch packet contains eight instructions.
In this code example we have a branch in parallel with the move K, then an add in parallel with a second add, in parallel with a multiply, and finally, a multiply in parallel with a load in parallel with a second load.

## Slide 41
Fetch Packet, VLIW
B
MVK
EP
ADD
ADD
MPY
EP
MPY
LD
LD
EP
Instruction
VelociTI Definitions
Notes: 41
Each group of parallel instructions is one execute packet, and the three execute packets are combined to create one fetch packet, an eight-instruction, or 256-bit very long instruction word.

## Slide 42
VelociTI Definitions
Fetch Packet: 8 32-bit instr (256 bits)
VLIW: Very Long Instr Word (256 bits)
EP: Execute Packet (group of || instr)
Instruction: 32-bit opcode
VelociTI: TI’s VLIW Architecture w/EPs
Notes: 42
So quickly reviewing the definitions, a fetch packet is eight 32-bit instructions. The VLIW is very long instruction word. EP, or execute packet, is a group of parallel instructions. Each instruction contains a 32-bit op code, and VelociTI is TI's VLIW architecture with execute packets.

## Slide 43
F1 D1 E1
F2 D2 E2
F3 D3 E3
CPU Type
Non-Pipelined
Pipelined
Clock Cycles
Pipeline full
Non-Pipelined / Pipelined CPU
1
2
3
4
5
6
7
8
9
F1 D1 E1
F2 D2 E2
F3 D3 E3
Notes: 43
Let’s examine non-pipelined versus pipelined CPUs, using a simple example, doing laundry. If we wanted to wash, dry, and fold several loads of laundry, we have three steps. If each step took 20 minutes, and we performed the tasks in serial fashion, in the first hour we would complete one load by washing it in the first 20 minutes, drying it in the second 20 minutes, and folding it during the final 20 minutes. At the end of 60 minutes, we would begin the second load of laundry. To complete three loads, we would spend 3 hours, or nine 20 minute cycles.
If the same task were completed in a pipelined fashion, during the first 20 minutes we would wash the first load, during the second 20 minutes we would dry load 1 and wash load 2, during the third 20 minute cycle, we would fold load 1, dry load 2, and washed load three. You can see from this simple analogy that we would complete our task in about half the time it took using a serial, or non-pipelined process.
This is how pipelining occurs in a CPU, and is demonstrative of the radical performance improvements that can be accomplished with optimized pipeline use.

## Slide 44
B .S1
MVK .S2
ADD .L1
ADD .L2
MPY .M1
MPY .M2
LD .D1
LD .D2
Serial Code Example
Notes: 44
Let’s examine several code examples going through the C6x pipeline.
Here we see a serial code example.There is a branch .S1, a move K dot S2, two adds, two multiplies, and two loads. Nothing is in parallel, so this is very much like the code we wrote earlier.

## Slide 45
Program Fetch
Decode
Execute
B
MVK
ADD
ADD
MPY
MPY
LD
LD
Pipeline Example (Fetch Packet)
PG
DP
DC
E1
-
E6
PS
PW
PR
Notes: 45
Let’s see what happens when this code, or this fetch packet, goes through the pipeline. While most pipelines consist of fetch, decode, and execute, the C6x pipeline breaks each major stage down into sub-stages.
The program fetch stage consists of four sub-stages: a PG or program generate sub-stage where the address of the fetch packet is generated, a PS or program send sub-stage where the address of the fetch packet is sent out to memory, a PW or program write sub-stage where we wait for the memory to send back the fetch packet, and a PR or program read sub-stage, where the instruction is actually read.
The decode stage of the pipeline has two sub-stages: DP or dispatch where the instruction is sent to the functional unit that's going to execute it, and DC or decode which will actually decode the instruction at the functional unit. It's at the dispatch stage that we figure out where the instruction is going to go. What's powerful about this is that it is not done in hardware. It’s done at compile or assemble time by the software tools. The tools are assigning the functional units, or in effect, scheduling the code.
The last stage is the execute stage. It's in this stage that the instruction is actually executed. The execute stage consists of sub-stages E1 through E6. The instruction is executed in E1,and E2 through E6 exist for the purposes of delay slots during which results of some instructions will be recognized.

## Slide 46
Program Fetch
Decode
Execute
ADD
ADD
MPY
MPY
LD
LD
MVK
B
+
FP5-2
Pipeline Code Example - Serial Execution
P
DP
DC
+
+
+
+
E1
E2
E3
E4
E5
E6
Notes: 46
Look at the pipeline code example for serial execution. The branch has been moved to the E1 phase, and the plus signs indicate the result, that is, the actual branch won't happen until the E6 stage. The move K is in the decode sub-stage of the pipeline, and the add and the remainder of the fetch packet are in the dispatch stage.

## Slide 47
MPY .M2
| | LD .D1
| | LD .D2
Partially Serial Code Example
B .S1
| | MVK .S2
ADD .L1
| | ADD .L2
| | MPY .M1
Notes: 47
Now lets examine a partially serial code example. In this case, we have three execute packets in our code.

## Slide 48
Decode
Execute
MPY
LD
LD
B
MVK
+
Partially Parallel Execution
DP
DC
+
+
+
+
E1
E2
E3
E4
E5
E6
ADD
ADD
MPY
Notes: 48
Examining the partially parallel execution in the pipeline, we see that the execute packets stay together, so we have branch and move K in the E1 stage. The two adds and the multiply are in the decode stage, and the multiply and the two loads are in the dispatch stage. So here each the components of each execute packet execute together in the pipeline.

## Slide 49
B .S1
| | MVK .S2
| | ADD .L1
| | ADD .L2
| | MPY .M1
| | MPY .M2
| | LD .D1
| | LD .D2
Fully Parallel Code Example
Notes: 49
Now let’s view a fully parallel code example. In this case, the fetch packet is equal to the execute packet. We’re fetching and executing eight instructions. The reason we can do this is that there are eight functional units on the device. So that's the most instructions that we can execute in parallel, eight.

## Slide 50
Decode
Execute
+
Fully Parallel Execution
DC
+
+
+
+
E1
E2
E3
E4
E5
E6
B
MVK
ADD
ADD
MPY
MPY
LD
LD
EP2
+
+
+
+
+
+
+
+
+
+
DP
Notes: 50
Look at fully parallel execution in the pipeline. Now the branch is in the E1 stage with the rest of that execute packet, ready to perform all eight instructions in parallel.
TI’s VelociTI architecture is able to achieve 1600 nativeMIPS by performing eight instructions in parallel.

## Slide 51
Programming the C62xx
Notes: 51
In this segment we will look at our coding example in C, linear assembly, and optimized C. We will see now how the tools put things in parallel for us, and then examine what the compiler and the linear assembler do, explaining the techniques used to parallelize the code, and get peak performance out of the C62xx.

## Slide 52
Objectives
Identify key software programs
Take our sum of products example through the code development process
Notes: 52
The objectives for this segment are to identify the key software programs in both the code generation and the debug process, and to take the sum of products example from the prior segment through the code development process.

## Slide 53
Programming the 'C62xx
Flow / Tools
70-80%
95-100%
100%
Linear ASM
Assembly
Optimizer
C
Compiler
Optimizer
Intrinsics
Typical
Efficiency
Coding
Effort
Low
Med
High
ASM
Hand
Optimize
Notes: 53
There are three ways that we can program the C6x. We can use C, linear assembly, and assembly.
When we program in C, we're using the C compiler, a separate pass optimizer, and intrinsics, which we'll describe a little later. Using this flow we can get 70 to 80 percent of the code efficiency of hand-optimized assembly with very little effort.
For linear assembly like our original code that we wrote without NOPs, the assembly optimizer tools will fill in delay slots for us, put things in parallel and create a very optimized piece of code, getting to 95 to 100 percent of the efficiency possible with hand optimized assembly, but with moderate effort.
With hand optimized assembly, we obviously get 100 percent efficiency, but the amount of effort required is much higher than using the software tools to optimize the code.

## Slide 54
Software Tool Flow
CL6x command invokes all tools
ASM6x
LNK6x
.obj
.out
.c
Link.cmd
.sa
Compiler
Asm Optimizer
Text
Editor
.asm
Notes: 54
The software tool flow begins with source code, and the text editor from which we could either create a C source, a linear assembly source, or a regular hand assembly source, which is a .asm file.
For a C source file, the extension is .c. We pass that source code through the compiler. For linear assembly source, we use the assembly optimizer, which creates an assembly language file. The assembly language file is then passed through the ASM6x assembler to create an object or .obj file. At this point, there are no physical addresses tied to either code or data, and the code is totally portable.
At the linker stage, the physical addresses for our code and data are assigned. The linker command file consists of two sections. The first is the memory map of the system which defines the type of memories we are using and where they reside. The second part of the linker command file is where we actually place our code and data in specific sections.
After linking, a .out or output file exists which can be debugged. All of these tools, the compiler, the assembly optimizer, the assembler and the linker are invoked by the CL6x command shell.

## Slide 55
Target
Board
EMU6x
HEX6x
.out
EVM6x
Software Only
Contains DSP
PCI Card
ISA card
No DSP
PC<-> Target
ROM
Prog.
SIM6x
Debug
Notes: 55
In the debug tool flow, the .out file is run through the debugger, and we could either use a software simulator (SIM6x) or an evaluation module with a DSP on it (EVM6x).
The debugger also resides on the XES510 emulator, so the debugger software is EMU6x. The XES510 is used to download the output file into the target system.
Another way of using the .out file is to pass it through the HEX6x utility, which converts it into EPROM programming format, after which a ROM programmer is used to burn an EPROM. This EPROM can be placed on the target board to run the code.

## Slide 56
Examine C implementation of Sum of Products
Use the C62xx compiler to compile dotP.c
Examine assembly output of compiler
Discuss C optimizations
Using the C62xx Compiler
Notes: 56
Now lets look at a C implementation of a sum of products. Using the 'C62xx compiler to compile dotP.c, we’ll examine the assembly output of the compiler and then we'll discuss some C optimizations.

## Slide 57
short dotP(short *m, short *n, short count)
{ int i;
short product;
short sum = 0;
for (i=0; i < count; i++)
{
product = m[i] * n[i];
sum += product;
}
return(sum);
}
Dot Product in ‘C’
Notes: 57
Here we see our sum of products example written in C.
The program is dotP and we're calling it on *m and *n pointers, which are short values, or 16-bit values. We also are passing an account of the number of times we're going to do the sum of products.
The loop is written as: for I equals zero and I less than count, perform the product M[I] times N[I], then sum that product with the previous product, until count equals to zero, then return the sum.

## Slide 58
C Source File
Compiler Tools
Assembler
Linker
C Optimizer
Code
Generator
.asm
-z
C Compiler
Run-time
Libraries
.out
Parser
.c
Notes: 58
To use the compiler tools on this C source file (dotP.c), the source goes through the parser which checks C syntax, then through the C optimizer which will optimize our C code, then to the code generator, which creates an assembly language file. This assembly language file is passed through the assembler, which creates an object file, then is linked to create an output file.
For the C environment, run-time support libraries are also linked. The run-time support libraries allow us to do things like initialization of variables and initializing the processor for the C environment.

## Slide 59
Invoking the Compiler/Linker
CL6x -g -o2 -k dotP.c -z -o dotP.out -l rts6201.lib
specify run-time library (small L)
-z invokes the linker
output file name
compiler options
compiler options: CL6x -g -o2 -k dotP.c
Notes: 59
To invoke the compiler and linker using the CL6x command, the command line would be CL6x minus g, minus o2, minus k, dotP.c.
Minus g, minus o2, and minus K are the compiler options that we're using and the file is dotP.c.
Everything after the minus z, shown here in white, communicates with the linker.

## Slide 60
Invoking the Compiler/Linker
-z invokes the linker -z -o
CL6x -g -o2 -k dotP.c -z -o dotP.out -l rts6201.lib
specify run-time library (small L)
-z invokes the linker
output file name
compiler options
Notes: 60
Minus z invokes the linker, minus o indicates the output file.

## Slide 61
Invoking the Compiler/Linker
output file name: dotP.out
CL6x -g -o2 -k dotP.c -z -o dotP.out -l rts6201.lib
specify run-time library (small L)
-z invokes the linker
output file name
compiler options
Notes: 61
The output file name is dotP.out.

## Slide 62
Invoking the Compiler/Linker
specify run-time library (small L) -l rts6201.lib
CL6x -g -o2 -k dotP.c -z -o dotP.out -l rts6201.lib
specify run-time library (small L)
-z invokes the linker
output file name
compiler options
Notes: 62
Minus LRTS62o1.lib is the run-time support library that we're using to do that initialization of the C environment.

## Slide 63
Options
Description
-g Enables src-level symbolic debugging
-s Interlist C statements into assembly listing
-o2 Invokes optimizer at second highest level
-k Keep assembly language file
Common Compiler Options
Notes: 63
We will be using some common compiler options in this code which are commonly used in a variety of situations.
The option minus g enables source-level symbolic debugging of our C code, which allows us to say "go main" and have the debugger know where main is and what it is.
Minus s, allows us to interlist C statements into the assembly listing. This allows us to see an intertwined relationship between lines of C and lines of assembly when we're debugging C code with assembly. In this case, we will see a line of C highlighted along with several lines of corresponding assembly. That's also useful when we want to debug C code.
Minus o2 invokes the compiler optimizer at the second highest level. Minus o3 is the highest level but minus o3 does file optimizations. This would be used if we had several files and wanted to compile them with the highest level of optimization. In our example, we have only one file.
Minus k keeps an assembly language file. In this segment we will examine the output of the compiler, which is an assembly language file. If we didn't use the minus k, it would automatically just call up the assembler and create an obj file. But since we want to see what type of code the compiler is generating, we will use the minus k option.

## Slide 64
Options
Description
-al Create assembler listing file
-as Retain asm symbols for debugging
Common Assembler Options
Notes: 64
Here we see options for the assembler, the ASM6x tool.
Minus L creates an assembler listing file, which would have a list of the opcodes with the assembly language statement.
Minus AS would return assembly symbols for debugging. This is useful, for instance, when we want to be able to find the symbol for a loop in the debugger.

## Slide 65
Options
Description
-z Invokes linker (lnk6x)
-o Output file name
-m Map file name
-l Link-in libraries (small -L)
Common Linker Options
Notes: 65
Looking at some common linker options, Minus z invokes the linker and the CL6x command file. Minus o is what we named the output file. Minus M creates a map file which will tell us where our code and data ended up in the memory map. And finally, minus L will link in our run-time support libraries.

## Slide 66
c0: ldh .D2 *B5++,B4
| | ldh .D1 *A4++,A0
c1: nop 1
c2: ldh .D2 *B5++,B4
| | ldh .D1 *A4++,A0
| | [B0] sub .L2 B0,1,B0
c3: [B0] B .S2 L3
c4: ldh .D2 *B5++,B4 | | ldh .D1 *A4++,A0
| | [B0] sub .L2 B0,1,B0
c5: mpy .M1x B4,A0,A3
| | [B0] B .S2 L3
c6: ldh .D2 *B5++,B4
| | ldh .D1 *A4++,A0
| | [B0] sub .L2 B0,1,B0
Notes: 66
Let’s look at theoutput of the compiler. When we run CL6x minus g, minus o2, minus k on that sum of products, this is the code that gets generated by the compiler. Here we see a preamble or prior to the loop,

## Slide 67
*** Two-Cycle Loop L3: add .L1 A3,A5,A0 | | mpy .M1x B4,A0,A3 | | [ B0 ] B .S2 L3 ext .S1 A0,16,16,A5 | | [ B0 ] sub .L2 B0,1,B0 | | ldh .D2 *B5++,B4 | | ldh .D1 *A4++,A0
Notes: 67
and, we have a two-cycle loop. So now we have two execute packets to create the loop instead of the 16 instructions we had before.
Let’s recognize what the C compiler has done to our code.

## Slide 68
Software Pipelining
Creates highly optimized loop-code
  Implements parallel instructions
  Fills delay slots
  Maximizes functional units
Implemented by tools
  Invoked with Compiler options -o2 or -o3
  Assembly Optimizer using .sa extension
Notes: 68
The C compiler is using a technique called software pipelining, which creates highly optimized loop-code. It implements parallel instructions, fills delay slots, and maximizes the use of the functional units.
This is implemented automatically by the tools when we invoke the compiler with the options minus o2 or minus o3, or when we use the assembly optimizer.

## Slide 69
Pipeline Example Code
LDH
LDH
MPY
ADD
How many cycles would it take to perform this loop 5 times?
(Disregard delay-slots).
| |
Notes: 69
To gain a better understanding of what software pipelining is, let’s do a pipeline example.
In contrast to hardware pipelining, where we were working on different instructions in different stages of the pipeline, in software pipelining, we're going to be working on different iterations of the loop.
In this pipeline example code, we see a load in parallel with another load, then a multiply followed by an add.
How many cycles would it take to perform this loop 5 times, disregarding delay slots?

## Slide 70
Pipeline Example Code
How many cycles would it take to perform this loop 5 times?
(Disregard delay-slots).
5 x 3 = 15
LDH
LDH
MPY
ADD
| |
Notes: 70
It takes 15 cycles to perform this loop 5 times. The two parallel loads take one cycle. There is a multiply, which takes a second cycle, and an add, which takes a third cycle.
To do this loop once takes three cycles, so to do it five times takes 15.

## Slide 71
Non-Pipelined Code
.M1
.M2
.L1
.L2
.S1
.S2
ldh
ldh
mpy
add
1
2
3
4
5
6
7
8
9
ldh
ldh
ldh
ldh
add
add
mpy
mpy
Cycle
Notes: 71
Let’s view our code example, first in a non-pipelined fashion.
In cycle one, we do the first load using the .D units. In the second cycle, I do the first multiply; in the third cycle, I do the first add; in the fourth cycle, I'm doing my second load; in the fifth, my second multiply; the sixth, my second add; in the seventh, the third load; the eighth, the third multiply; and then the ninth, the third add.
So here we're just looking at three iterations of the loop taking nine cycles. If we showed all 5 iterations, we would see it would take 15 cycles to do this loop in non-pipelined fashion.
It is also apparent the functional units are not being used very much. For instance, the .D units are used in cycles 1, 4 and 7, but not in 2, 3, 5, 6, 8, or 9.

## Slide 72
Pipelining Code
.M1
.M2
.L1
.L2
.S1
.S2
.D1
.D2
Notes: 72
Let’s see what happens when this code is pipelined using the software pipelining technique. We start with all the functional units, the two D units, the two M units, the two L units and the two S units.

## Slide 73
Pipelining Code
1
ldh
Cycle
ldh
.M1
.M2
.L1
.L2
.S1
.S2
Notes: 73
In cycle one, we do a parallel load of the first values.

## Slide 74
Pipelining Code
1
2
ldh
Cycle
ldh
ldh
ldh
.M1
.M2
.L1
.L2
.S1
.S2
mpy
Notes: 74
In cycle two, we do the first multiply and the second load.

## Slide 75
Pipelining Code
1
2
3
ldh
Cycle
ldh
ldh
ldh
ldh
ldh
.M1
.M2
.L1
.L2
.S1
.S2
mpy
mpy
add
Notes: 75
In cycle three, we do the first add, second multiply, and third load.

## Slide 76
Pipelining Code
1
2
3
4
ldh
Cycle
ldh
ldh
ldh
ldh
ldh
ldh
ldh
.M1
.M2
.L1
.L2
.S1
.S2
mpy
mpy
mpy
add
add
Notes: 76
In cycle four, we see the second add, third multiply, and fourth load.

## Slide 77
Pipelining Code
1
2
3
4
5
ldh
Cycle
ldh
ldh
ldh
ldh
ldh
ldh
ldh
ldh
ldh
.M1
.M2
.L1
.L2
.S1
.S2
mpy
mpy
mpy
mpy
add
add
add
Notes: 77
In cycle five, we see the third add, fourth multiply and fifth load.

## Slide 78
Pipelining Code
1
2
3
4
5
6
ldh
Cycle
ldh
ldh
ldh
ldh
ldh
ldh
ldh
ldh
ldh
.M1
.M2
.L1
.L2
.S1
.S2
mpy
mpy
mpy
mpy
mpy
add
add
add
add
Notes: 78
In cycle six, we see the fourth add and the fifth multiply, but no loads. Why are there no loads?

## Slide 79
Pipelining Code
1
2
3
4
5
6
ldh
Cycle
ldh
ldh
ldh
ldh
ldh
ldh
ldh
ldh
ldh
.M1
.M2
.L1
.L2
.S1
.S2
mpy
mpy
mpy
mpy
mpy
add
add
add
add
Notes: 79
Our code had five loads and five multiplies. After five cycles we've completed all the loads, and there are no more to do.

## Slide 80
Pipelining Code
1
2
3
4
5
6
7
ldh
Cycle
ldh
ldh
ldh
ldh
ldh
ldh
ldh
ldh
ldh
.M1
.M2
.L1
.L2
.S1
.S2
mpy
mpy
mpy
mpy
mpy
add
add
add
add
add
Notes: 80
In cycle seven, we seethe fifth and last add.
By pipelining the code, instead of taking 15 clock cycles to do this loop, it took only seven clock cycles or less than half the time.
We saw different iterations of the loop, so if we look at step four, or in cycle four, we saw the second add, the third multiply, and the fourth load. We were working on different iterations of the loop and that's why when we saw the compiler output, we saw a several loads before the first multiply.

## Slide 81
Further Optimization of C Code
Intrinsics
Word Wide Throughput
Notes: 81
There are some further optimizations that we will now discuss: intrinsics, and word wide throughput.

## Slide 82
Comparing Coding Methods
C Code
y = a * b
C Code Using Intrinsics
y = _mpy (a, b);
In-Line Assembly
asm (“ MPY A0, A1, A2”);
Notes: 82
Comparing coding techniques, if in C code we wanted to do a product, we can do Y is equal to A times B, and that’s what the C code looks like.
C code using intrinsics is different in syntax. We write this as Y equals underscore MPY, so the MPY instruction we saw before, is the assembly instruction to do the multiple. The underscore MPY is making this an intrinsic so it can be used from C but still use the assembly multiply. Also, the intrinsic is being called on A and B, so still in the C environment and using variables instead of registers. However, we are now getting the power of the assembly language statement.
For in-line assembly, within C code, simply write ASM and then bracket, quote, MPY A0 A1 A2, close quote, close bracket, semicolon. In-line assembly is ignored by the compiler. It disrupts the C environment. The compiler ignores it and will move code around it, which is not always desirable.
Using C code with intrinsics allows us to remain in the C environment, yet get the power of using almost an in-line assembly call.

## Slide 83
Intrinsics vs. In-Line Assembly
Can use C variable names instead of register names
Are compatible with the C environment
Adhere to C’s function call syntax
Intrinsics...
Notes: 83
So comparing intrinsics versus in-line assembly, intrinsics can use C variable names instead of register names, they are compatible with the C environment, and they adhere to the C's functional call syntax, so they look just like C.

## Slide 84
List of Available Intrinsics
Intrinsics
_mpylh
_mpyhl
_nassert ( )
_norm
_sadd
_set
_add2
_clr
_ext/u
_lmbd
_mpy
_mpyh
_smpy
_sshl
_ssub
_subc
_sub2
_sat
Notes: 84
This list shows variety of intrinsics available on the C6x. The two that we're going to concentrate on for our sum of products are the underscore MPY and the underscore MPYH.
MPY does a 16 by 16 multiply, so it does the 16 lower bits of a register times the 16 lower bits of the register.
MPYH takes the upper 16 bits of the register and multiplies that value by the upper 16 bits of the register. We'll see in a moment how we can take advantage of that in our sum of products example.

## Slide 85
Word-Wide Optimization in C
Access 32-bit data by declaring data as 32-bit type
Perform numerical operations using intrinsics
Notes: 85
Beyond the use of intrinsics, we can also use word-wide optimizations to enhance performance.
In word-wide optimizations, since we have the ability to load 32-bit values, we can access 32-bit data by declaring the data as a 32-bit type.
In our C code before, we were calling them shorts; they were 16 bits, bringing them in 16 at a time. But the external bus is 32 bits, so we can take advantage of that by loading words, then performing the numerical operations using the intrinsics _MPY and _MPYH.

## Slide 86
Optimizing - Using LDW
a0
a1
. .
x0
x1
. .
a1
a0
Memory
Registers
x1
x0
A0
A1
x
=
LDW...
LDW...
?
Notes: 86
In memory, I had values A0 through A1, which were 16-bit values. Using load-word, its possible to get A0 and A1, two 16-bit values, in a 32-bit register.
For A1, we want to load word on X, so X0 and X1, are in by-16 memory, and we pull that into a 32-bit register. Now we have X0 in the lower half of the register and X1 in the high half of the register.

## Slide 87
a1
a0
x1
x0
A0
A1
x
=
a1 x1
a0 x0
A3
A7
+
a1x1 + a0x0
LDW .D1 *A5++,A0
LDW .D1 *A6++,A1
MPY .M1 A0, A1, A3
MPYH .M1 A0, A1, A7
ADD .L1 A3, A7, A4
A4
Optimizing - Using LDW/MPYH
*
*
Notes: 87
We use MPY and MPYH to perform the multiply.
In A3, we multiply A0 times X0 and put the result in A3 with the instruction MPY.M1 A0 A1, A3.
We can also use the second multiplier with an MPYH. Here I'm using the same one, .M1 A0 A1 A7. This multiplies the upper 16 bits in A0 by the upper 16 bits in A1 and puts that result in A7.

## Slide 88
short dotP(int *m, int *n, short count)
{ short i;
int productl, int producth;
short suml = 0, short sumh=0, short sum=0;
for (i=0; i < count; i++)
{productl = _mpy (m[i],n[i]);
suml += productl;
producth = _mpyh(m[i],n[i]);
sumh += producth; }
sum = suml+ sumh;
return(sum);
}
Optimized Dot Product in ‘C’
Notes: 88
Now we're going to rewrite our C code knowing that we can use word-wide optimizations and can take advantage of the fact that we do have two multipliers on this DSP.
We have declared * M and * N not as shorts, but as 32-bit values, calling them "int’s”. We have created product L and a product H, and now can do a low product and a high product. The sum has been broken into high and low components, sumL and sumH.
For the loop, we’ll say product L is equal to underscore MPY M sub I times N sub I, and we are getting the lower 16 bits and then summing L. Next we sum the lower product using sum L plus/equals product L. Similar syntax is used with an underscore MPY H to obtain the high product, producth.
Finally, since we are computing two multiplies in the loop, we no longer need to iterate 40 times. Instead we loop 20 times. When we have completed the loop, we get the final sum by adding the low sum to the high sum, and returning this value.

## Slide 89
Create linear assembly code
Use optimizing assembly tool
Examine the output of optimizing assembly tool
Using the C62xx Assembly Optimizer
Notes: 89
The C6x has a new tool called the assembly optimizer, which we will now explore. We will create linear assembly code, use the optimizing assembly tool, then examine the output of the optimizing assembly tool.

## Slide 90
Linear Assembly Using Sum of Products
loop: ldh *p_m++, m
ldh *p_n++, n
mpy m, n, prod
add prod, sum, sum
[count] sub count, 1, count
[count] b loop
No functional unit specifications
No registers specified
No NOPs
Notes: 90
Looking at the linear assembly sum of products, notice that we don't specify any functional units. For instance, we do a load H but do not indicate the need for the .D unit.
No registers are specified, no A0, A1, etc., and we keep the syntax at a symbolic level. Also, there are no NOP instructions. The assembly optimizing tool is going to do this all for us. What we will find is that there won’t be any NOPs because the tools will optimize this loop so well.

## Slide 91
dotp: dotProc a4, b4, a6, b3
.reg p_m, m, p_n, n, prod, sum, count
mv a4, p_m
mv b4, p_n
mv a6, count
loop: .trip 40
ldh *p_m++, m
ldh *p_n++, n
mpy m, n, prod
add prod, sum, sum
[count] sub count, 1, count
[count] b loop
mv sum,a4
.endproc a4, b3
Notes: 91
Here we see the dotP linear assembly program in its proper format. The .Proc says this piece of code is to be sent to the assembly optimizer. We begin the code with .Proc and end it with the .endproc. This defines the scope of the assembly optimizer over this piece of code.
On that . proc line, we indicate the registers that contain any arguments this code receives. In this case, another function is passing me arguments in A4, B4, A6 and B3.
The dot REG line declares the registers we will use in our code. Here we have a pointer to M, a pointer to N, M and N themselves, and the product, sum and count.
Since another function is sending me arguments, we need to assign those arguments to the registers. We indicate here that we are being passed a pointer of M in A4, so we use a move A4 P underscore N. Similar syntax is used for the other arguments.
We indicate the number of times we’ll need to go through the loop using dot trip 40 to show the minimum number of loop iterations. At the end of the loop, we pass the final sum out to another function using move sum into A4. And for the N product, we pass A4 out to the other function.

## Slide 92
Invoking Assembly Optimizer
Invokes:
Optimizing Assembler and Assembler
Linker command file
CL6x -gs -als dotp.sa -z file.cmd
Notes: 92
Now lets invoke the assembly optimizer using the CL6x command. We use the CL6x with options minus G and S which provides the symbolic debug, minus als to create an assembly listing file, called dotP.sa.
The .sa extension shows that this is linear assembly and I'm sending this piece of code to the assembly optimizer.
Minus Z talks to the linker, which links dotP .sa when it's finished with the linker command file, in this case, file.cmd.

## Slide 93
c0: ldh .D2 *B5++,B4
| | ldh .D1 *A0++,A3
c1: ldh .D2 *B5++,B4
| | ldh .D1 *A0++,A3
| | [B0] sub .L2 B0,0x1,B0
c2_3_4: ldh .D2 *B5++,B4
| | ldh .D1 *A0++,A3
| | [B0] sub .L2 B0,0x1,B0
| | [B0] B .S2 c7
c5_6: ldh .D2 *B5++,B4
| | ldh .D1 *A0++,A3
| | [B0] sub .L2 B0,0x1,B0
| | [B0] B .S2 c7
| | mpy .M1x B4,A3,A4
Notes: 93
Look at the linear assembly output that is produced, we have C0 and C1, C2, 3 and 4 are repeats, so those four lines of code, or that execute packet, is actually repeated four times.

## Slide 94
*** Single-Cycle Loop
c7: ldh .D2 *B5++,B4 || ldh .D1 *A0++,A3 || [B0] sub .L2 B0,1,B0 || [B0] B .S2 c7 || mpy .M1x B4,A3,A4 || add .L1 A4,A5,A5
Notes: 94
We can see that this is a completely optimized piece of code. The tools have eliminated all no NOP instructions, and we have a single-cycle loop executing six instructions.
We also notice a .M1x. What this is showing is that we can multiply data from the B register file and the A register file together. The X indicates a cross path. So I'm multiplying a B register by an A register and I put the result in the A register. In fact, we could have up to two cross paths: one from B to A and one from A to B.

## Slide 95
Learn how to invoke the simulator
Take a look at the user interface
Benchmark our last code example
Using the C62xx Simulator
Notes: 95
Let’s learn how to invoke the simulator from the command line. Inside the debug segment, we’ll also look at the user interface again. We’ll review all the pull-down menus and all the windows in the debugger, then debug our last code example, which is the linear assembly.

## Slide 96
Invoking the Simulator
SIM6x file.out
Notes: 96
To invoke the simulator, we type SIM6x file.out.

## Slide 97
Benchmarking Code Results
Non-optimized 657 clock cycles
Assembly
Generic C 120 clock cycles
Optimized C 84 clock cycles
with Intrinsics
Linear Assembly 63 clock cycles
Notes: 97
Our final tools demo will show the linear assembly benchmark. Its impressive to note that we were able to reduce the number for clock cycles by an order of magnitude by using the software tools with linear assembly code.