## Slide 1
High-Performance Communications Market
Performance
Power
‘C6x
‘C54x
Single Channel
  Client side
  Subscriber side
  Terminal side
Multi–Channel
  Server side
  Central Office
  Basestation
Notes: In the high-performance communications marketplace, the C54x has traditionally been viewed as supporting the single-channel applications while the C6x is being viewed as the optimal solution for the multi-channel application. For instance, using this concept, the C6x would be the best choice for basestations, central office switches, and other “server-side” end-equipments. The C54x, on the other hand, would target the handset, modem, PBX, or other “terminal-side” end-equipments. The C54x is optimized for “low power” while the C6x is optimzed for “highest performance”. The dotted lines above refer to the areas of influence that these respective processors will impact. You will notice some overlap. This is intended to show that in many applications, there are tradeoffs in what the end-equipment requires and the processor delivers. As a result, beyond the obvious solutions of cellular phone (C54x) and very large multi-channel basestation (C6x), it becomes less obvious what is the best solution for other high-performance telecommunications applications. Key attributes and end-equipment careabouts need to be defined to better evaluate these solutions.

## Slide 2
Key Attributes
Performance 1.0 5.0
Power 115 mW 3 W
Price (25Ku) $33 $96
Packaging 12x12 mm 35x35 mm
Coding Assembly “C”
C54x C62x
Notes: Five of the key attributes that can be used to identify the best solution for the C54x vs. the C6x are: performance, power, price, packaging, and primary coding methodology. The performance ratio of C6x vs. C54x is 5-to-1. While there is a 10x improvement of the C6x versus typical 16-bit architectures in use today (C5x, 16xx from Lucent, etc.), there is a 5-times improvement of C6x over C54x. The power dissipation of the C6x is estimated to be about 3W. The C54x power dissipation for 100 MIPS device is projected at 115 mW. How is 115 mW determined? If you consider the 100 MIPS LC549 (which uses a 2.5V core, 3.3V I/O), the calculation would be: (2.5V)(.45 mA/MIPS)(100 MIPS) = 112.5 mW. If you consider a 66 MIPS LC548 with a 3.0V core, the calculation would be (3.0)(.6 mA/MIPS)(66 MIPS) = 118 mW. The C54x is optimized for lower power dissipation. The price of 25Ku LC548 or LC549 is around $33, while the C6x is about $97, which represents roughly a 3-to-1 ratio. The BGA (ball grid array) package of the C6x is 352 pins and is 35mm x 35mm, while the LC549 will be offered in a 144-pin BGA (called microStar BGA) that is 12mm x 12mm. The primary coding methodology for the C54x is assembly since it has a very efficient architecture for dense code size. The primary coding methodology for the C6x is “C” since the C6x is a highly efficient “C” engine.

## Slide 3
Case Study #1
Voice communicator with paging & data messaging
  Small, portable, wireless
Requires 68 MIPS
Key Careabouts:
  low power
  small size
  minimized external memory accesses
Notes: Case Study 1:
A customer is considering the design of a small, portable, wireless device. The application is intended to act as a voice communicator with paging and data messaging capabilites integrated as well. The customer has stated that his application will require approximately 68 MIPS. The key careabouts of the design are small size and low power dissipation. In addition, integration is very important and external memory accesses must be minimized. Which processor makes the most sense for this customer: C54x or C6x?

## Slide 4
Case Study #1
80 MIPS LC549
  32K words of RAM, 16K words of ROM
  3 serial ports, host port interface
(80 MIPS) x (.6 mA/MIPS) x 3.0V =
108 mW
IDLE 1, 2, 3 modes ; PLL options
Size: micro*BGA = 12 x 12 x 1.4 mm
Notes: For case study #1, the straightforward answer is the C54x. The device choice would need to include the integration of both memory and peripherals on-chip. This is based on the requirement to minimize the power (off-chip accesses increase power dissipation) and minimize space (off-chip memories require large system space). While a large ROM device may be best suited for this application, the LC549 also provides large memory and peripheral integration. The LC549 utilizes 32K words of RAM and 16K words of ROM, one time-division multiplexed serial port, two buffered serial ports, and a host port interface. An 80 MIPS device operating at 3.0V would dissipate just over 140 mW using on-chip resources (assumes 0.6 mA/MIPS). This mA/MIPS number will move to .45 mA/MIPS in the next process technology node. The LC548 and LC549 have three power down modes (IDLE1, IDLE2, IDLE3). IDLE1 dissipates 31.2 mW (@ 80 MIPS), IDLE2 dissipates 9.6 mW), and IDLE3 dissipates 1.65 mW. These numbers assume that the PLL is enabled. If the PLL is enabled there are 31 different options to multiply the external clock (e.g. a x4 PLL would allow a 20 Mhz external clock to drive 80 Mhz, and hence 80 MIPS, on-chip. The small size of the LC549 BGA package (12x12x1.4) enables small system size.

## Slide 5
Case Study #2
Basestation for digital cellular network
Want to reduce system cost & size
No previous TI DSP experience
Key careabouts:
  density of channels
  low power (somewhat concerned)
  development cycle time / ramping TI DSP learning curve
Notes: Case Study 2:
Company X is developing their next generation basestation for a digital cellular network. They have no past experience with TI DSP and are looking at reducing both the cost and size of their existing system. Their chief careabout is density of channels, but this is not without some concern about power consumption. They would like to move forward on this design as quickly as possible. Since they have some code investment already on another architecture, they are a little worried about the learning curve of a new architecture. However, a competitively superior solution for their product is most important. Which processor, C54x or C6x, makes the most sense for this customer?

## Slide 6
Case Study #2
C62xx C54x
# of channels 60 60
(EFR GSM algorithm)
# of channels / DSP 30 6
# of DSPs 2 10
DSP total cost $192 $330
$ / channel $3.20 $5.50
Notes: For case study #2, the goal is to implement 60 channels of enhanced full-rate GSM. This would be two E1 spans. Looking at the C54x, EFR GSM requires approximately 16 MIPS to implement. This means that 60 channels would necessitate ten 100 MIPS C54x devices (each implementing six channels). The DSP price of this solution would be $330 (10 * $33) and the $ / channel would equal $5.50 ($330/60 channels). Taking the 5:1 performance ratio into consideration shows that the C6x can implement five times the number of channels per DSP. This translates to two C6201 devices to handle the channel requirements. The DSP cost ($96 per 6201) would be $192 and the per channel cost is $3.20. For this application, where #’s of channels (channel density) is the primary concern, the C6x clearly has the lower cost per channel for this system. Therefore, since this is the #1 careabout, the C6x is the best solution. The requirement for “moving up the learning curve” quickly can be handled by the excellent C Compiler of the C6x.

## Slide 7
Case Study #3
Next gen pico-basestation for PCS network
  operates at 1.8 (or 1.9) GHz
Smaller effective range
  requires more basestations
  requires significant size & cost reductions
Reduced number of channels and power consumption budget
Notes: Case Study 3:
Company Y is developing their next generation pico-basestation for a PCS (Personal Communications Services) network. PCS cellular operates at 1.8 (or 1.9) Ghz vs. the 800-900 Mhz range for digital cellular. As a result, more information can be transmitted with PCS, but since the effective range is much smaller, more basestations are required to maintain the signal strength. While there are more basestations, the size and cost of each must be reduced significantly compared to standard digital cellular basestations. The number of channels and power consumption budget is reduced as well. Which processor, C54x or C6x, makes the most sense for this customer?

## Slide 8
Case Study #3
C62xx C54x
# of channels 24 24
(EFR GSM algorithm)
# of channels / DSP 24 6
# of DSPs 1 4
DSP total cost $ 96 $132
$ / channel $4.00 $5.50
mW / channel 125 mW 20 mW
Notes: Case study #3 focuses on a smaller basestation with a lower channel requirement, smaller size, lower cost, and lower power. In this case, taking the same algorithm (for ease of comparison) that was used in case study #2, it would require four 100 MIPS LC54x devices to implement the required 24 channels. The total processor cost is $132 and the cost per channel is $5.50. The power dissipation (mW per channel) would be 20 mW. This is determined by: 4 x 115 mW = 460 mW. 460 mW / 24 channels is approximately 20 mW per channel. For the C6x, only one 6201 is required (and is not even fully utilized). This produces a processor cost of $96 and $ / channel of $4. The power dissipation is determined by: 3W (or 3000 mW) divided 24 channels = 125 mW / channel. For this application, either choosing the C54x or the C6x is a viable alternative. The C6x has a better cost per channel number ($4 vs. $5.50) while the C54x has a lower power dissipation per channel figure. It depends on what are the most important careabouts for the customers.

## Slide 9
Equalization 7
Channel code / decode 7
Vocoder compress/decomp 13
Echo canceller 2 - 4
Total 29 - 31
30 MIPS / channel
3 channels for 100 MIPS
Case Study #3
Function for C54x MIPS
Notes: In some of these case studies, we have been considering only the vocoder portion of GSM. It may be more realistic to look at all the DSP algorithm requirements for an application like a pico-basestation. In this case, one full-duplex channel of, say IS-54B could require 7 MIPS for equalization (receive side), another 7 MIPS for the channel coding and decoding (receive & transmit sides), 13 MIPS for vocoder compression and decompression (VSELP for receive and transmit), and 2-4 MIPS for the echo-canceller (receive side). This equates to 3 full-duplex channels (30 MIPS each) on a 100 MIPS LC54x.

## Slide 10
Case Study #3
C62xx C54x
# of channels 24 24
(all DSP functions)
# of channels / DSP 12 3
# of DSPs 2 8
DSP total cost $192 $264
$ / channel $8.00 $11.00
mW / channel <250 mW <40mW
Notes: Applying the calculations from the previous slide, 24 full-duplex channels would require eight 100 MIPS C54x’s. The total C54x processor cost would be $264, $11 per channel, and only 38.3 mW / channel. For the C6x, we assumed a 4X improvement in performance vs. C54x. This number was not 5:1 ratio vs. C54x in this case because we want to present the realistic idea that while theoretically the number of channels will fit onto a C6x from a performance standpoint, there is some question of whether the memory requirements of more than 12 channels per DSP can be met. This is meant as a exercise to show that there are 3 factors that must be considered with respect to # of channels: 1) what is maximum # of channels that will “fit” on the DSP from a performance standpoint; 2) what is the maximum number of channels that can be handled from a memory standpoint; 3) what is the maximum number of channels that can be handled taking I/O limitations into consideration. In this case, considering 12 channels, the DSP processor cost / channel of the C6x is significantly better than the C54x ($8 / channel vs. $11 / channel). However, the C54x has a much better power / channel number. Once again, the consideration must be made as to whether channel density is number 1 issue or a combination of factors.

## Slide 11
Case Study #4
Processor for network telephony server
Key algorithms: G.728, G.729, G.723, low level data & fax modem code
Existing design uses 16 40-MIP C5x’s
Key careabouts:
  greater performance
  lower power & cost
  smaller system size
  supporting 30 vocoder channels
Notes: Case Study 4:
Company W is in the early processor consideration phase for a network telephony server. This particular piece of equipment performs telephony functions across a network. The key algorithms of interest for this application are vocoders like G.728, G.729, and G.723 and some low level data & fax modem code. There is interest in supporting 30 vocoder channels per system. The existing design uses sixteen 40 MIPS C5x devices. This customer would like to optimize his next generation design by achieving greater performance, lower power, lower cost, and a reduction in the size of his system. Which processor, C54x or C6x, makes the most sense for this customer?

## Slide 12
Case Study #4
Sixteen 40 MIPS C51 devices per system (15 for 15 channels, 1 for cntrl)
2 boards of 15 DSPs handle 30 channels
Cost: 30 x $22 = $660 ($22 / channel)
Power: ~ 380 mW / channel
Space: 576 mm2 per channel
Notes: In this application, a network telephony server, the requirement is to handle 30 vocoder channels (like G.728, G.729, G.723, etc.). The previous design used 16 C51 devices, each channel requires one 40 MIPS DSP. The desire is to implement 30 channels (one E1 line) in the system. One C51 per channel and 1 C51 acts as a controller for the board (16 total). The DSP cost of the existing system is around $660 (30 C51s * $22). This results in a per channel cost of $22. The power consumption per channel is around 380 mW (5V x 1.9 mA/MIPS x 40 MIPS). Each C51 is in a 24mm x 24mm package. This translates to 576 mm2 per channel. While this does not consider the routing of the 132 pins, the number is useful for rough comparisons to new alternatives. Overall, the “benchmarks” to beat in the new system are: $22 per channel, 380 mW / channel, and 576 mm2 per channel.
The new design needs to be smaller, cheaper, and lower power dissipation.

## Slide 13
Case Study #4
C62xx C54x
# of channels 30 30
(G.728 or 723 + fax)
# of channels / DSP 12 3
# of DSPs 3 10
DSP total cost $288 $330
$ / channel $9.60 $11.00
mW / channel <300 mW 40mW
Space / channel 122.5mm2 65mm2
Notes: Taking a look at this application, we are looking at implementing 30 channels of an application like G.723 + V.29 fax or G.728. For this application, we have approximated a 30 MIPS requirement at any one time. While there are multiple algorithms that are needed for this system, G.723 requires about 16.6 MIPS on a C54x and low-level fax or modem code will not be above 14 MIPS. As a result, a total of about 30 MIPS is anticipated which means that ten 100 MIPS C54x’s are required to handle 30 channels. This translates to $330 cost and $11.00 / channel. The power dissipation would be around 40 mw / channel (computed on prior case study) and the space requirement is 65 mm2. For the space requirements, we used 14mm x 14mm which equals 196 mm2. (10 x 196 mm2) / 30 channels = 65.3 mm2. First, why 14mm x 14mm, when the package is only 12mm x 12mm? To be more realistic, we have accounted for some of the routing of the DSPs beyond the package itself. For the C6x, the number of channels that can be handled by the C6x is about 12 per DSP, once again lower than the theoretical performance number of 15 due to memory requirements. This means that 3 C6201’s are not being fully utilized (3 x 12 = 36). In this case, the $ / channel is slightly in favor for C6x and power / channel is in favor of C54x. Either solution is superior to the existing design; it is a tradeoff of careabouts.

## Slide 14
Case Study #5
Enterprise server application
  multiple v.34 modems (Rockwell)
  DTMF & echo cancellation (ASIC & i960 RISC processor)
Want systems functions combined into same physical chasis
Unsure if can/should be condensed to single board
Notes: Case Study 5:
Company Z has alot of processor experience, but not necessarily with DSP. They are developing a piece of networking equipment that is described as an "enterprise server" which requires the use of multiple V.34 modems as well as DTMF (Dual-Tone Multi-Frequency) and echo cancellation. They have looked at various ways to implement this solution. Today, they are using banks of Rockwell modems to perform the V.34. The functionality of the DTMF and echo cancellation is currently addressed by a different piece of equipment with a combination of ASIC and an i960 RISC processor. They would like to combine the functionality of the entire system into the same physical chasis -- something that is not possible today due to size of 'stack & rack' modems they currently use. The new system probably cannot be condensed to a single board and there is some argument that they would like these separate for future flexibility and scalability. Cost, power, performance, size, and ease of use are all key considerations for this design. Which processor, C54x or C6x, is the better choice for this design?

## Slide 15
Case Study #5
C62xx C54x
# of channels 30 30
(V.34 modem datapump)
# of channels / DSP 15 3
# of DSPs 2 10
DSP total cost $192 $330
$ / channel $6.40 $11.00
mW / channel 200 mW 40mW
Space / channel 82mm2 65mm2
Notes: This case study follows the format of previous ones by looking at the tradeoffs associated with power dissipation, cost, performance. It is by looking at these attributes that will help determine whether this is a C54x or a C6x socket. Other factors, like coding methodology, could come into play. Since this particular customer has not used DSP before, they may be reluctant to code in assembly. If this is the case, while the C54x has an excellent C Compiler, the C6x is the leader in ease of use and efficiency with respect to assembly. In this case, the task is to implement 30 channels which would require ten 100 MIPS C54x’s, each handling 3 channels. The total processor cost is $330, which translates to $11.00 per channel. The mW / channel is 40 mW ((115 mW x 10) / 30 = 38.3 mW). The space required is 65 mm2 computed by ((14 mm x 14 mm) x 10) / 30. The C6x can handle 15 modems per 6201 which means that two 6201s would be needed to handle the E1 span (30 channels). The total C6x processor cost is $192, the cost per channel is $6.40, the power per channel is 200 mW, and the space is 82 mm2. As the graphic shows, the C6x is definitely the better choice from the cost per channel perspective. The power per channel and the space per channel are very comparable to the C54x. As a result, for the modem portion of this application would best be suited as a C6x application.

## Slide 16
Case Study #5
C62xx C54x
# of channels 30 30
(echo cancellation + DTMF)
# of channels / DSP 30 15
# of DSPs 1 2
DSP total cost $96 $66
$ / channel $3.20 $2.20
mW / channel 100 mW 8 mW
Space / channel 41 mm2 10 mm2
Notes: In this “enterprise server” the customer wanted to separate the modem functions from the other DSP functions (echo cancellation and DTMF). One of the reasons for this was for scaling purposes and also since they wanted to use the modem boards (without DTMF and echo cancellation) in other end-equipment applications. DTMF and echo cancellation require about 6 MIPS on a C54x. This would necessitate the use of two 100 MIPS C54x devices to handle the 30 channels -- each DSP would take 15 channels. The processor cost for the two C54x’s would be $66 and the $ per channel would be $2.20. The mW per channel is under 8 mW and the space per channel is around 10 mm2. This application (echo cancellation and DTMF) utilizes only about one-third of the performance offered by one C6201. Therefore, the cost per channel, power per channel, and space per channel are all higher for the C6x in this case. As a result, this application would be best suited for the C54x. However, the customer would need to commit to the code development on two processors. If this is not acceptable, it may make more sense to try and integrate the functionality of the echo cancellation and DTMF onto the modem board (depends upon how adamant the customer is to keeping these apps separate).